## Slide 1: Wayforward on NW based CRS-IM RRM for Legacy UE
Intel
3GPP TSG-RAN WG4 RAN#86bis
Melbourne, Australia, 16 – 20 Apr, 2018
R4-1804209
Document for: Approval

## Slide 2: Warm-up and cool-down mechanism for legacy UE
The criteria for warm-up and cool-down subframes design is that it should guarantee that CRS muting is fully transparent to legacy UE and will not cause any degradation to legacy UE.
  Legacy UE means the R14-and-earlier UE.
  The warm-up and cool-down subframe design for RACH and SI reading shall be release independent.
Scenario | Mode | Warm-up subframes | Cool-down subframes | Other full BW CRS occasions
All configured paging occasions | IDLE, CONNECTED | 6 | 1 | All paging occasions
SI acquisition (SIB1 and SI-window) | IDLE, CONNECTED | 6 | 1 | All SI reading windows(incl. SIB1 and all other SIBs)
Prior to RA transmission occasions | IDLE, CONNECTED | 6 | 0 | In Connected mode from RAR window to HO complete; In IDLE mode, from RAR window to RRC configuration complete
Msg2 monitoring duration | IDLE, CONNECTED | 6 | 1 | 
Msg4 monitoring duration | IDLE, CONNECTED | 6 | 1 | 
On-duration of CDRX | CONNECTED | 10 | 6 | During active time
SR over PUCCH in CDRX | CONNECTED | 6 | 1 | From UE SR-over-PUCCH to the corresponding UL grant reception
RSTD measurement | CONNECTED | 6 | 0 | All RSTD measurement occasions
Table 1. Warm-up and cool-down mechanism summary for legacy UE