## Slide 1: Way forward on Measurement gaps
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #86bis Melbourne, Australia, 16th – 20th April, 2018
Agenda item: 7.9.3.2
R4-1804761

## Slide 2: Way forward
In RAN4#86 meeting, WF R4-1803118 was approved to further study some remaining issues. However a scenario is never discussed:
  When serving cells in LTE/FR1 and measurement objects in both LTE/FR1 and FR2 is the measurement object.
For this scenario, we suggest that
  MN shall indicate per-UE gap
    -For UE only capable of per-UE gap, or
    -For UE capable of per-FR gap however the measurement gap is needed on LTE/FR1 carriers due to restricted baseband processing resources (whether measurement gap is needed for per band combination is specified in RAN2);
    -UE fulfils the measurement requirements of FR2 based on the configured measurement gap pattern.
  • MN shall not configure measurement gap:
    -For UE capable of per-FR gap and there is no baseband restriction.
    -UE fulfils the measurement requirements of FR2 based on effective MGRP 20ms.