## Slide 1: WF for RF requirements for UL MIMO
Qualcomm, []
R4-1805132
3GPP TSG-RAN WG4 Meeting #86
Melbourne, Aus, 16-20 Apr, 2018
Agenda item: 7.4.6.10 [FR1] Coherent UL MIMO

## Slide 2: Background
RF requirements for coherent UL MIMO have been discussed for the past few meeting in RAN4.
The goal has been to define a spec for phase and power error drift from the last SRS transmitted over a time window.
Some of the documents discussed in RAN4 are:
  R4-1805109, UE RF Requirements for ULMIMO, 3GPP TSG-RAN4 #86, Melbourne, Aus, 16-20 Apr, 2018
  R4-1802327, Coherent UL MIMO: UE Spec Limits on Gain and Phase Imbalance, 3GPP TSG-RAN4 #86, Athens, GR, 26 Feb – 2 Mar, 2018.

## Slide 3: Way Forward
For UL MIMO, relative power and phase difference between the two chains is of importance.
The goal of the spec is to ensure that UE can maintain a power and phase error within a bound for a period of time after every SRS transmitted.
Power and phase error shall be measured as:
  A delta between the power and phase difference between the two chains computed at the last SRS and at any other time after that within the time window specified.
The time window specified is a guide to the gNB to determine the SRS periodicity for UL MIMO UE

## Slide 4: Way Forward
Proposed spec for phase error, power error and the time window is:
Phase error | Power error | Time window
¦ error ¦ ≤ 40 degrees | ¦ error ¦ ≤ 4 dB | At least 20 msec
Time window starts after the symbol in which SRS is sent.
  20 msec has been derived from 40 slot SRS periodicity and 30kHz SCS assumption

## Slide 5: Way Forward
Conditions under which its difficult to compute this error:
  When SRS RB configuration is different from that of data
    As the phase and power error of the FE filters changes over frequency
    The average phase and power error computed for SRS and that of the data will be different causing an inherent bias in error
    Hence, for the purposes of test, SRS RB configuration shall be the same as the of the data.
  When SRS is sounded on each antenna at a different slot
    Computation of reference for power and phase error creates an inherent bias in error
    Hence, for the purposes of the test, SRS shall be sounded in the same slot and same symbol on both the antennas.
  When SRS is transmitted in multiple symbols in a slot with frequency hopping between them
    Computation of reference for power and phase error becomes confusing
    Hence, for the purposes of test, single SRS with the same RB configuration of that of data shall be sent on both the chains at the same time.

## Slide 6: Way Forward
Conditions under which these requirements do not need to be met:
  If within that 20 msec window from the last SRS, UL MIMO is disabled
    In this case at least one of the Tx chains is disabled.
    So when the UL MIMO is re-enabled within that 20 msec and Tx chain is re-enabled, then phase error of the PLL cannot be bounded.
But if the UL MIMO is active for the entire window:
  The phase error spec still applies during all UL slots within the window.