## Slide 1: Wayforward on requirement of intra-frequency measurement without gap
Mediatek, Huawei, HiSilicon,
3GPP TSG-RAN WG4 RAN#86 Bis
Melbourne, Australia, April 16th- 20th, 2018
R4-1805521
Document for: Approval

## Slide 2: Background : requirement of Intra-frequency measurement without gap agreed in #86 (updated after ad-hoc session)
Sub-Issue | 
Intra-frequency PSS/SSS Sync. | Agreement: FR1 max(600ms,[5] x SMTC period) FR2 max(600ms, ,[5] xN1x SMTC period) Editor’s note: The values of N1 are to be updated.
Intra-frequency SBI Acquisition | Agreement: FR1 max(120ms, 3 x SMTC period) FR2 max(200ms, [5] x N2 x SMTC period) Editor’s note: The values of N2 are to be updated.
Intra-frequency Measurement | Agreement: FR1 max(200ms, 5 x SMTC period) FR2 max(400ms, 5 x N3 x SMTC period) Editor’s note: The values of N3 are to be updated.
  Agreement for single frequency layer

## Slide 3: Background : agreed measurement types in R4-1801829
All the UE activities for consideration (all the activities are SSB based)
  RLM
  Measurement type A: Intra-frequency measurement w/o MG and w/o interruption
    For FR1, no mixed numerologies is assumed for this measurement type
    For FR2, this measurement type is not applicable
  Measurement type B: intra-frequency measurement with interruption
    For FR1, mixed numerologies is assumed for this measurement type
    For FR2, Rx beam sweeping is assumed for this measurement type
  Measurement type C: intra-frequency measurement with MG
    E.g. Intra-frequency measurement outside active BWP
  Measurement type D: inter-frequency measurement and inter-RAT measurement

## Slide 4: Background : agreed measurement types in R4-1801829
  All the scenarios for consideration
    Fully overlapped scenarios:
      Scenario 1a: Fully overlapped between MG and SMTC in type A
      Scenario 1b: Fully overlapped between MG and SMTC in type B
      Scenario 1c: Fully overlapped between MG and RLM
    Partial overlapped scenarios:
      Scenario 2a: Partial overlapped between MG and SMTC in type A
      Scenario 2b: Partial overlapped between MG and SMTC in type B
      Scenario 2c: Partial overlapped between MG and RLM
    Fully non-overlapped scenarios:
      Scenario 3a: Fully non-overlapped between MG and SMTC in type A
      Scenario 3b: Fully non-overlapped between MG and SMTC in type B
      Scenario 3c: Fully non-overlapped between MG and RLM
  In partial overlapped scenarios 2a/2b/2c, the requirements can be further divided into 9 cases
FR1/FR2 | Within MG only | within/outside MG | Outside MG only
2a(Type A) | NA for FR1 (Note-1) | FFS for FR1 (Note-1) | FFS for FR1 (Note-1)
2b(Type B) | FFS for FR1/FFS for FR2 | FFS for FR1/FFS for FR2 | FFS for FR1/FFS for FR2
2c(RLM) | NA for FR1/FFS for FR2 | FFS for FR1/FFS for FR2 | FFS for FR1/FFS for FR2
*Note-1: There is no Type-A measurement in FR2, hence the corresponding requirements aren’t needed |  |  | 

## Slide 5: Background : ad-hoc meeting agreement
  Tuesday evening ad-hoc meeting
    Clarification on Type C: intra-frequency measurement with MG
      For intra-frequency measurement, as long as BWP is switched to not cover the intra-frequency target cell SSB frequency during the measurement period, this measurement shall be considered as intra-frequency measurement with gap(type C).
    FR1:
      Partial overlap between RLM and MG, RLM requirements only consider ALL the RLM-RS which is not overlapped with MG.
      All MG will be used for measurement for (type C and D) for scenario 2a/2b.
      Type A/type B measurement will only be conducted outside the measurement gap for Scenario 2a/2b.
      In FR1, 2a, 2b and 2c are conducted only outside the MG.
  Wednesday afternoon ad-hoc meeting
    For misalignment of DRX and SMTC
      Applicable DRX cycle periodicities ≤ 320ms
      Relaxation factor 1.5
      Applied generically so there will be no condition in the spec on misalignment
       Requirement will be scaled by 1.5 when DRX cycle periodicities ≤ 320ms

## Slide 6: Scope of this Wayforward
Discuss the requirement considering
  Multiple NR serving cells
  Collision between SMTC occasions and MG
    Scenarios to be first focused on
      2a and 2b when measurement is conducted only outside the MG.
        The requirement for “2a and 2b when measurement can also be conducted within the MG” can be later extended, if RAN4 reaches consensus on whether to specify the corresponding requirements
      The requirements of 3a can be simplified from that of 2a
    Other scenarios to be discussed after RAN4 reaches consensus on whether to specify the corresponding requirements
      1a and 1b
      3b
  Different DRX cycles
  Misalignment between DRX on duration and SMTC window

## Slide 7
  The requirement of single frequency layer is further scaled by the parameter Kca which is a carrier-specific scaling factor, considering the multiple frequency layers
    Kca = 1, for the target frequency layer with NR PCell and NR PSCell.
    Kca = [TBD], for the target frequency layers with NR SCells.
      The value may refer to the RAN4 conclusion on scaling/grouping rules of inter-frequency measurement.
Requirement with multiple NR serving cells (CA/EN-DC)

## Slide 8
  When intra-frequency measurements are performed in SMTC occasions not overlapped with the gaps
    When RLM-RS is partially overlapped with SMTC occasions
      Requirement for for a single serving cell considers the parameter Kp-intra
        Kp-intra is a scaling factor multiplied with required sample number
        Kp-intra = 1/(1- SMTC period /MGRP), where SMTC period < MGRP
    When RLM-RS is fully overlapped with SMTC occasions
      RAN4 is to study sharing mechanism for RLM and intra-frequency measurement (according to evening ad-hoc agreement in R4-1805513)
  When intra-frequency measurements can also be performed in SMTC occasions overlapped with the gaps
    Whether to specify the requirement is FFS
Requirement of 2a and 2b when measurement is conducted only outside the MG

## Slide 9
  Applicability of non DRX and DRX requirement should be specified based on below 3 different DRX cycles
    When DRX is not in use
    When DRX is in use and DRX cycle ≤ 320ms
    When DRX is in use and DRX cycle > 320ms
  Requirement considers the different DRX cycles

## Slide 10
  Requirement of single frequency layer considers the parameter Kmis
    Kmis is a scaling factor multiplied with required sample number
      Kmis = 1, when DRX is not in use
      Kmis = 1.5, when DRX is in use and DRX cycle ≤ 320ms
      Kmis = 1, when DRX is in use and DRX cycle > 320ms
  Requirement considers the misalignment between SMTC window and DRX on duration

## Slide 11
  Examples for information
    Scenarios 2a and 2b when measurement is conducted only outside the MG, and RLM-RS is partially overlapped with SMTC occasions
  Requirement of intra frequency measurement without gap for non-DRX
Sub-Issue | Requirement | Applicable measurement type
Intra-frequency PSS/SSS Sync. | FR1 max( 600ms, Ceil(Kp-intra x [5])x SMTC period x Kca ) | A, B
 | FR2 max( 600ms, Ceil(Kp-intra x [5]) x N1 x SMTC period x Kca ) | B
Intra-frequency SBI Acquisition | FR1 max( 120ms, Ceil(Kp-intra x 3) x SMTC period x Kca ) | A, B
 | FR2 max( 200ms, Ceil(Kp-intra x [5]) x N2 x SMTC period x Kca ) | B
Intra-frequency Measurement | FR1 max( 200ms, Ceil(Kp-intra x 5) x SMTC period x Kca ) | A, B
 | FR2 max( 400ms, Ceil(Kp-intra x 5) x N3x SMTC period x Kca ) | B

## Slide 12
  Examples for information
    Scenarios 2a and 2b when measurement is conducted only outside the MG, and RLM-RS is partially overlapped with SMTC occasions
    Requirement of intra frequency measurement without gap for DRX cycle ≤ 320ms
Sub-Issue | Requirement | Applicable measurement type
Intra-frequency PSS/SSS Sync. | FR1 max[ 600ms, Ceil(Kp-intra x 1.5 x [5])x max(DRX cycle, SMTC period) x Kca ] | A, B
 | FR2 max[ 600ms, Ceil(Kp-intrax 1.5 x [5]) x N1 x max(DRX cycle, SMTC period) x Kca ] | B
Intra-frequency SBI Acquisition | FR1 max[ 120ms, Ceil(Kp-intrax 1.5 x 3) x max(DRX cycle, SMTC period) x Kca ] | A, B
 | FR2 max[ 200ms, Ceil(Kp-intrax 1.5 x [5]) x N2 x max(DRX cycle, SMTC period) x Kca ] | B
Intra-frequency Measurement | FR1 max[ 200ms, Ceil(Kp-intrax 1.5 x 5) x max(DRX cycle, SMTC period) x Kca ] | A, B
 | FR2 max[ 400ms, Ceil(Kp-intrax 1.5 x 5) x N3x max(DRX cycle, SMTC period) x Kca ] | B

## Slide 13
  Examples for information
    Scenarios 2a and 2b when measurement is conducted only outside the MG, and RLM-RS is partially overlapped with SMTC occasions
    Requirement of intra frequency measurement without gap for DRX cycle > 320ms
Sub-Issue | Requirement | Applicable measurement type
Intra-frequency PSS/SSS Sync. | FR1 Ceil(Kp-intra x [5])x DRX cycle x Kca | A, B
 | FR2 Ceil(Kp-intrax [5]) x N1 x DRX cycle x Kca | B
Intra-frequency SBI Acquisition | FR1 Ceil(Kp-intrax 3) x DRX cycle x Kca | A, B
 | FR2 Ceil(Kp-intrax [5]) x N2 x DRX cycle x Kca | B
Intra-frequency Measurement | FR1 Ceil(Kp-intrax 5) x DRX cycle x Kca | A, B
 | FR2 Ceil(Kp-intrax 5) x N3x DRX cycle x Kca | B