## Slide 1: Way forward on BWP Switching
Ericsson, Intel, Mediatek, Nokia, Nokia Shanghai Bell, Huawei, HiSilicon…
3GPP TSG-RAN WG4 Meeting # 86bis
Melbourne, Australia, April 16-20, 2018
R4-1805540

## Slide 2: Background
The bandwidth part (BWP) switching delay for the following 4 BWP reconfiguration scenarios was agreed in an LS out in R4-1803283 as summarized in the table below:
  Scenario 1: The reconfiguration involves changing the center frequency of the BWP without changing its BW. The reconfiguration may or may not involve changing the SCS.
  Scenario 2: The reconfiguration involves changing the BW of the BWP without changing its center frequency. The reconfiguration may or may not involve changing the SCS.
  Scenario 3: The reconfiguration involves changing both the BW and the center frequency of the BWP. The reconfiguration may or may not involve changing the SCS.
  Scenario 4: The reconfiguration involves changing only the SCS, where the center frequency and BW of the BWP remain unchanged.
Frequency Range | Scenario | Type 1 Delay (us) | Type 2 Delay (us) | Comment
1 | 1 | 600 | 2000 | 
 | 2 | 600 | 2000 | 
 | 3 | 600 | 2000 | 
 | 4 | 400 | 950 | No delay required from the RF perspective
2 | 1 | 600 | 2000 | 
 | 2 | 600 | 2000 | 
 | 3 | 600 | 2000 | 
 | 4 | 400 | 950 | No delay required from the RF perspective

## Slide 3: Agreements
BWP switching on a NR serving carrier (carrier1) will cause interruption in at least serving carrier1.
If it is identified that BWP switching in NR serving carrier(s) will cause interruption on LTE serving carrier(s) in EN-DC then the interruption on LTE serving carrier(s) shall be specified in terms of subframes.

## Slide 4: Issues for Investigation
Investigate whether or not BWP switching for the 4 BWP reconfiguration scenarios on cell1 will also cause interruption:
  on LTE PCell and LTE activated SCell(s) and other NR serving cells (e.g. PSCell, SCells) in EN-DC,
  on other NR serving cells (e.g. PCell, SCells) in NR CA.
Investigate suitable interruption duration (in number of symbols or slots) on NR serving cell(s) due to BWP switching.
Investigate for scenario where BWP switching results in change of the SCS from old SCS (SCS1) to a new SCS (SCS2), whether the time unit (number of symbols or slots) to express interruption time is based on SCS1 or SCS2.
Investigate whether there is any problem for the UE to transmit and/or receive signals in one or more time resources (symbols or slots) occurring immediately after the interruption time due to BWP switching e.g.
  any impact on channel estimation,
  any possible impact on measurements,
  analysis to identify other possible impacts is not precluded.
Investigate whether BWP switching due to change in only baseband parameter(s) without changing LO, RF BW or SCS will cause any interruption and the interruption time (if the procedure is supported and the interruption occurs).
  Additionally investigate if changing baseband parameters without BWP switch will need interruptions (if the procedure is supported).

## Slide 5: Annex A: RAN1 agreement in RAN1#91 for information
Agreements:
  A UE is not expected to receive DL signals or transmit UL signals during the transition time of active DL or UL BWP switch
    For DCI-based active BWP switch, from RAN1 perspective, the transition time of active DL or UL BWP switch is the time duration from the end of last OFDM symbol of the PDCCH carrying the active BWP switch DCI till the beginning of a slot indicated by K0 in the active DL BWP switch DCI or K2 in the active UL BWP switch DCI
    For timer-based active BWP switch, from RAN1 perspective, the transition time of active DL or UL BWP switch is the time duration from the beginning of the subframe (FR1) or from the beginning of the half-subframe (FR2) immediately after a BWP timer expires till the beginning of a slot UE is able to receive DL signals or transmit UL signals in the default DL BWP for paired spectrum or the default DL or UL BWP for unpaired spectrum