## Slide 1: WF on measurement gaps for dense PRS
Ericsson
3GPP TSG-RAN WG4 Meeting #86bis R4-1805556
Melbourne, Australia, 16th - 20th April, 2018
Agenda Item: 6.18.4.4

## Slide 2: New gaps and RSTD measurements
A new measurement gap pattern is configured for UE that requires such gaps for performing RSTD measurements
Impact on RSTD requirements:
  The existing UE Cat M1 and Cat M2 accuracy requirements for RSTD measurements in gaps shall also apply with the new gaps
  RAN4 to check whether the existing UE Cat M1 and Cat M2 measurement period requirements (generically formulated with respect to MGL and MGRP) for RSTD measurements in gaps also apply with the new gaps

## Slide 3: New and legacy measurement gap patterns
Observation: currently in LTE
  the network can configure one per-UE measurement gap pattern
  UE can indicate one per-UE measurement gap pattern or per-CC measurement gap patterns
FFS whether legacy measurement gap patterns can be used in parallel with new gaps, choose between options:
  Option 1: using the earlier configured leagacy gaps shall be suspended during the RSTD measurement period (while new gaps are used) and resumed after the RSTD measurements are complete (when new gaps are no longer used)
  Option 2: the legacy gaps may be used during the RSTD measurement period, in parallel with new gaps (the details are FFS)
FFS gap alignment between legacy measurement gap and new RSTD measurement gap

## Slide 4: New gaps and RRM measurements
New measurement gap patterns shall not be requested for RRM measurements
FFS using the new gaps (when configured for RSTD) for RRM during the RSTD measurement period, choose between options:
  Option 1: new gaps shall not be used for RRM measurements
  Option 2: new gaps may be used for RRM measurements, under certain conditions (conditions FFS)
Impact on RRM requirements:
  RAN4 to discuss the impact of new gaps on RRM requirements, including intra-frequency and inter-frequency RRM requirements

## Slide 5: New measurement gap patterns
The UE shall indicate the preferred measurement gap pattern (corresponding to their MGL and MGRP specified in 36.133), not only the need for gaps
Candidate new measurement gap patterns:
Other measurement gap pattern configurations are not precluded
Gap Pattern Id | MGL (ms) | MGRP (ms) | Applicability | Note
rstd0 | 6 | 40 | Only for CE Mode A | Agreed
rstd1 | 10 | 80 |  | Agreed
rstd2 | 10 | 160 |  | Agreed
rstd3 | 10 | 320 |  | Agreed
rstd4 | 10 | 640 |  | Agreed
rstd5 | 10 | 1280 |  | Agreed
rstd6 | 14 | 160 |  | Agreed
rstd7 | 14 | 320 |  | Agreed
rstd8 | 14 | 640 |  | Agreed
rstd9 | 14 | 1280 |  | Agreed
rstd10 | 32 | 320 | Only for CE Mode B | Agreed
rstd11 | 32 | 640 | Only for CE Mode B | Agreed
rstd12 | 32 | 1280 | Only for CE Mode B | Agreed
rstd13 | 54 | 640 | Only for TDD with CE Mode B | FFS
rstd14 | 54 | 1280 | Only for TDD with CE Mode B | FFS
rstd15 | 64 | 640 | Only for measuring a cell based on two PRS configurations | FFS
rstd16 | 64 | 1280 | Only for measuring a cell based on two PRS configurations | FFS
rstd17 | 80 | 640 | Only for measuring a cell based on three PRS configurations | FFS
rstd18 | 80 | 1280 | Only for measuring a cell based on three PRS configurations | FFS