## Slide 1: WF on output power requirements on FR2
Samsung, Verizon, Vodafone, AT&T, Ericsson, Nokia, Deutsche Telekom, Telecom Italia, T-Mobile USA, SoftBank, Telstra, US Cellular, CMCC, DISH Network, C Spire, NXP, MTI, Reliance Jio, IITH, IITM, CEWiT, Tejas Networks, Bluetest, Etisalat, Fraunhofer HHI, Fraunhofer IIS
R4-1805768
3GPP TSG-RAN WG4 Meeting #86bis
Melbourne, Australia, 16 - 20 April 2018
Agenda item: 7.4.8.1

## Slide 2: Background: min peak EIRP
In the last meeting, there are two WFs on min peak EIRP
  R1-1803372 WF on output power requirements on FR2 Qualcomm, Samsung, Verizon, AT&T, T-Mobile USA, NXP, DISH, Orange, ZTE, US Cellular, C Spire, Ericsson, Telstra, KT, Nokia, Vodafone, Mavenir, Telecom Italia, Reliance Jio, IITH, IITM, CEWiT, Tejas Networks
  R1-1803460 WF on FR2 peak EIRP for handheld UE Intel, Xiaomi, OPPO, vivo, MediaTek, LGE, Apple, Qorvo
Two predominant proposals were 23.2 dBm and 22 dBm. If further compromise is made, the average would be 22.6dBm

## Slide 3: Background: min peak EIRP
Data reported according to R4-1804123
More than one data point for the same material have been provided by the same company
Excluding the higher data point for the same material from the same source, the average for 28GHz is 22.3 dBm; and for 39GHz, it is 20.2dBm
Source | Min Peak EIRP [dBm] 28 GHz | Min Peak EIRP [dBm] 39 GHz
Intel (glass 1) | 20.20 | 18.40
Intel (glass 2) | 19.70 | 17.90
LGE [13] | 21.50 | 18.30
MediaTek | 21.05 | 20.45
Huawei | 22.30 | 19.70
Samsung | 22.40 | 20.60
Intel alt. design (glass 1) | 20.30 | 18.50
Intel alt. design (glass 2) | 19.80 | 18.00
Motorola | 21.70 | 18.60
Qualcomm (plastic) | 26.24 | 24.74
Qualcomm (glass) | 25.24 | 23.44

## Slide 4: Background: Spherical coverage
Company | - | Samsung [2] | Apple [3] | LGE [4] | Sony [5] | MediaTek [6] | Qualcomm [7]
Frequency range | - | n257 |  |  |  |  | 
Display | Partial / Full | Full | Full | Full | Full | Full | Full
Side cover (cover material near antennas) | Metal / Plastic | Metal | Metal | Metal | Metal | Metal | Glass
%-tile point | dBm | Decreased by (from 100%-tile) |  |  |  |  | 
EIRP @ 50% | dB | 8.6 | 14 | 12.5 | 13 | 11.6 | 5.5
EIRP @ 40% | dB | 10.4 | 15 | 14.5 | 15 | 12.2 | 6.3
EIRP @ 30% | dB | 12.4 | 17.5 | 16 | 16 | 12.8 | 8
EIRP @ 20% | dB | 15 | 21 | 18.5 | 18 | 13.5 | 10.2
[2] R4-1800990, “Further efforts on EIRP CDF for spherical coverage,” Samsung, RAN4-AH-1801, Jan 2018
[3] R4-1713850, “Consideration of EIRP spherical coverage requirement,” Apple, RAN4#85, Nov 2017
[4] R4-1803982, “Revised NR UE peak EIRP and Spherical EIRP levels at mmWave,” LGE, RAN4#86B, Apr 2018
[5] R4-1805321, “UE Spherical coverage at mmWave 28GHz,” Sony, RAN4#86B, Apr 2018
[6] R4-1801594, “EIRP CDF Simulation Analysis for Spherical Coverage,” MediaTek, RAN4#86, Feb 2018
[7] R4-1804587, “On UE Spherical Coverage With Glass Packaging,” Qualcomm, RAN4#86B, Apr 2018

## Slide 5: Way Forward
For Rel-15
  For 28GHz
    Min peak EIRP is 22.4 dBm
    50%-tile requirement for EIRP CDF is 13.8 dBm, 8.6 dB down from peak (above)
  For 39GHz
    Min peak EIRP is 20.6 dBm
    50%-tile requirement for EIRP CDF is FFS
For Rel-16
  Strive to specify 20%-tile requirement for EIRP CDF in Rel-16