## Slide 1: Way forward on FR2 EVM requirements for QPSK, 16QAM and 64QAM
Huawei, Nokia, NTT DOCOMO, INC., […]
3GPP TSG RAN WG4 #86BIS Meeting R4-1805803
Melbourne, Australia, 16 – 20 April, 2018

## Slide 2: Background: EVM for FR2 BS
Modulation scheme for PDSCH | Required EVM [%]
QPSK | [17.5 – 19]%
16QAM | [12.5 – 14]%
64QAM | [8 – 9]%
In Table 9.6.2.3-1 in TS 38.104, EVM requirements for BS type 2-O carrier is still put with a range of values in square brackets.
In RAN4# 86 bis, The following contribution were discussed
  R4-1804959, Draft CR to TS 38.104 clause 9.6.2.3 – EVM requirements for BS type 2-O, Source: Nokia, Nokia Shanghai Bell
  R4-1803935, EVM requirements for FR2, Source: Huawei, HiSilicon
  R4-1804985, EVM Equalizer Requirements for FR2, Source: Ericsson

## Slide 3: Options discussed in RAN4#86bis
Modulation scheme for PDSCH | Option 1: Required EVM [%] | Option 2: Required EVM [%] | Option 3: Required EVM [%]
QPSK | 17.5% | 19% | [17.5 – 19]%
16QAM | 12.5% | 14% | [12.5 – 14]%
64QAM | 8% | 9% | [8 – 9]%

## Slide 4: Background: EVM for FR2 UE
Parameter | Unit | Average EVM Level (%) | Reference Signal EVM Level (%)
Pi/2 BPSK | % | 30 | 30
Pi/2 BPSK with pulse shaping | % | 30 | 30
QPSK | % | [17.5] | [17.5]
16 QAM | % | [12.5] | [12.5]
64 QAM | % | 8 | 8
Table 6.4.2.1.1-1: Minimum requirements for Error Vector Magnitude
Table 6.4.2.1-1 in TS 38.101-2: Minimum requirements for Error Vector Magnitude

## Slide 5: WF
Modulation scheme for PDSCH | Required EVM [%]
QPSK | [17.5 %]
16QAM | [12.5 %]
64QAM | [8 – 9%]
FR2 EVM requirements for FR2 BS are updated as following Table.
The following values are dependent on the specifics such as performance loss, EVM equalizer, EVM window definitions to be discussed in RAN4#87
RAN4 will make decision on FR2 BS EVM requirements in RAN4 #87.