## Slide 1: WF on NR BS TAE for inter-BS
NTT DOCOMO, INC.
R4-1805804
3GPP TSG-RAN WG4 Meeting #86bis
Melbourne, Australia, 16-20 April 2018
Agenda Item: 7.6.2.4.2.3

## Slide 2: Background
Following contribution triggers the discussion of understanding regarding TAE requirements for MIMO or TX diversity, and intra-band C CA.
  R4-1805339 NR BS TAE for distributed MIMO deployment scenarios NTT DOCOMO, INC.
  Background can be found in above document.
This document summarizes the Agreements/WF on NR BS TAE requirement for inter-BS.

## Slide 3: Agreements(1/2)
Following table shows the common RAN4 understanding of current TAE requirement applicability. (Discussion is required for yellow parts)
In RAN4#87 meeting, encouraged companies provide their understanding and view on following questions/action points.
  If the current TAE requirements (65ns for MIMO/Div. for both FR1/FR2, 260ns for intra-band C CA for FR1, and 130ns for intra-band C CA for FR2) are also applicable for inter-BS case?
  If the answer in 1. is “NO”, if RAN4 needs to specify separate TAE requirement for inter-BS case? If needed how RAN4 should derive the required TAE value?
In RAN4#87 meeting, RAN4 shall decide/have consensus on at least above 1 question, and agree the clarification CR to TS38.104 if needed.
Configurations | TAE requirement | 
 | Intra-BS | Inter-BS
MIMO or Tx div. | 65ns | ??
intra-band C CA | 260ns (FR1), 130ns (FR2) | ??

## Slide 4: Agreements(2/2)
Following table shows the common RAN4 understanding of current TAE requirement applicability. (Discussion is required for yellow parts)
In RAN4#87 meeting, encouraged companies provide their understanding and view on following questions/action points.
  If the current TAE requirements (3us for intra-band NC CA for both FR1/FR2, 3us for inter-band CA for both FR1/FR2) are also applicable for inter-BS case?
  If the answer in 1. is “NO”, if RAN4 needs to specify separate TAE requirement for inter-BS case? If needed how RAN4 should derive the required TAE value?
Configurations | TAE requirement | 
 | Intra-BS | Inter-BS
intra-band NC CA | 3us | ??
inter-band CA | 3us | ??