## Slide 1: Spectrum Situation and proposals to RAN4 in Rel 15
KT, SK Telecom, LG Uplus
ETISALAT, Ericsson, ZTE , Huawei
R4-1806020
3GPP TSG-RAN WG4 Meeting #86bis
Melbourne, Australia, 16-20 April 2018

## Slide 2: Korean Spectrum Auction
Below two spectrum ranges will be allocated to three Korean operators by auction which is scheduled to June 2018
  3,420 ~ 3,700 MHz (Total 280MHz, 10MHz resolution)
  26.5GHz ~ 28.9GHz (Total 2.4GHz, 100MHz resolution)
Korean operators have plan to start NR based commercial service in early 2019 based on Rel 15 standard

## Slide 3: Middle East and UAE Status
Certain ME markets (e.g. UAE) has two operators, where 90MHz CBW is planned be assigned within N41 to one operator
N78 spectrum availability for 5G NR deployment in ME markets is impacted by other terrestrial and satellite systems currently operating within portions of the band. 90MHz CBW is also considered for early deployment considering existing operating systems and GB requirement
Etisalat plans to deploy N78 as early as 2018 and N41 is planned in 2019
The 90MHz CBW needs to be supported in Rel. 15 for both BS and UE specifications as follow:
  90MHz CBW is agreed for BS specification in TS 38.104 for N78 and N41
  90MHz CBW needs to be specified for UE specification for N78 and N41 and to be harmonized with BS specification

## Slide 4: Proposal
Proposal 1: Specify 90MHz channel BW in Rel 15 for the UE to be harmonized with BS specification (TS 38.104)
  1-1: Define 90MHz for UE channel BW in n78 in Rel 15
  1-2: Define 90MHz for UE channel BW in n41 in Rel 15
Proposal 2: for n78 Intra band contiguous CA, below combo should be included in Rel 15
  100MHz+10MHz