## Slide 1: Way forward on UE TA offset for FDD and TDD in NR
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 #86bis Meeting
Melbourne, AU, 16th – 20th April, 2018
R4-1804614
Document for: Approval
Agenda item: 7.9.9.3

## Slide 2: Background
At the RAN4#86 meeting, following contributions were discussed and some agreements were made.
  R4-1803020 Timing advance offset Qualcomm
    It was agreed that N_TA-offset does not depend on the subcarrier spacing.
    The WF in R4-1803504 was discussed and noted.
  R4-1802750 TA offset for TDD LTE-NR coexistence Ericsson
    The LS in R4-1803570 was approved and sent to RAN2 (CC: RAN1).
    The draft CR in R4-1803139 was discussed and noted.
  R4-1802031 Way forward on UE TA offset for FDD and TDD in NR NTT DOCOMO, INC.
    It was agreed that RAN4 concludes on the proposal to apply same N_TA-offset value between FDD and TDD within the same frequency range in RAN4#86bis.

## Slide 3: Background
In R4-1802031, the issue of TA handling in case of FDD-TDD UL CA is discussed.
  In LTE, due to different NTA offset value between FDD and TDD, TA handling at network and at UE are complicated when TDD-FDD UL CA is introduced
    In FDD PCell and TDD SCell case:
      UE applies PCell UL transmit timing on SCell (i.e., follows NTA with NTA offset = 0 even on TDD cell)
      Network needs to signal NTA on FDD PCell so that NTA >= NTA offset (624)
      On FDD PCell, NTA for each of all other UEs also needs to be adjusted due to UE with FDD-TDD UL CA
    In TDD PCell and FDD SCell case:
      UE applies PCell UL transmit timing on Scell (i.e., follows NTA with NTA offset = 624 even on FDD cell)
      For other UEs on FDD SCell, network needs to signal NTA so that UL reception timings are aligned between UE with TDD-FDD UL CA and other UEs

## Slide 4: Discussion
Possible solution:
  Same NTA offset value between FDD and TDD within the same frequency range should be applied.
    According to the principle in agreed LS (R4-1803570), NTA offset value in LTE-NR coexistence band needs to be aligned with LTE specification.
    With this solution, complicated TA handling can be avoided except for the case with FDD-TDD UL CA including LTE-NR coexistence band
  As proposed in R4-1803020, NTA offset values should be integer multiple of natural sampling rate of all possible bandwidth
Frequency range and band of cell used for uplink transmission | NTA offset
FR1 except for LTE-NR coexistence bands | 25600
FR1 LTE-NR coexistence bands (FDD) | 0
FR1 LTE-NR coexistence bands (TDD) | 39936
FR2 | [13600]

## Slide 5: Proposal
Apply same NTA offset value between FDD and TDD within the same frequency range
  Table 7.1.2-2 in TS38.133 is updated as below
Frequency range and band of cell used for uplink transmission | NTA offset
FR1 except for LTE-NR coexistence bands | 25600
FR1 LTE-NR coexistence bands (FDD) | 0
FR1 LTE-NR coexistence bands (TDD) | 39936
FR2 | [13600]