## Slide 1: TDD UL/DL configuration for UE REFSENS and performance tests
Agenda Item: 7.5.10, 7.12.1
Source: Ericsson
Document for: Discussion
3GPP TSG-RAN WG4 Meeting #87
Busan, 21st– 25th May, 2018
R4-1806119

## Slide 2: Previous agreement for FR1
In R4-1805717 it’s agreed as following for FR1
    For FR1, the following TDD/HARQ configurations are applied for NR REFSENS requirements
      Semi-static TDD configuration
      UL/DL pattern
        FFS: TDD configuration for LTE side in EN-DC combinations (whether to apply the same configuration as NR side)
        FFS: Different TDD pattern between EN-DC and other scenario
      K0 = [0]
        FFS: K1 and max number of HARQ process
SCS | Alt.1 | Alt.2 | Alt3 | Alt4
15kHz | Aligned with LTE config #2 (5ms periodicity) |  |  | 
30kHz | {0, 33, 0, 41} (Option 3 in R4-1803445) | Aligned with LTE config #2 (5ms periodicity) | {0 0 0 32 1} with 2.5ms periodicity | {0 0 0 12 1} with 2.5ms periodicity
60kHz | {0, 33, 0, 41} (Option 3 in R4-1803445) | Aligned with LTE config #2 (5ms periodicity) | LTE config #2 with 1.25ms periodicity | {0 0 13 1} with 1ms periodicity

## Slide 3: Previous agreement for FR2
For FR2, semi-static TDD configuration
Postpone the discussion for FR2 to RAN4 #87
K0 = [0]
    FFS: K1 and max # of HARQ process

## Slide 4: Proposals for FR1
Strong motivation and clear benefit to align the frame start with LTE when it comes to EN-DC deployment for FR1.
    For REFSENS tests use DDDSU to align with LTE TDD UL/DL config 2
      HARQ process can be reduced e.g. 4 than max number.
    For UE performance tests use “phase approach” to gradually introduce more TDD config during performance phase.
      Phase 1 for first round simulation alignment uses DDDSU with 5ms periodicity and max HARQ process, targeting for agreement in July Adhoc (Alt 2 for all SCSs)
        At least for 15kHz and 30kHz SCS
      Phase 2 includes more TDD config (Alt 1, Alt 3 and 4)

## Slide 5: Proposals for FR2
For REFSENS tests the purpose is to verify noise figure is properly handled by UE side in a minimum performance level, which doesn’t involve deployment plan
    Use DDDSU to align with LTE TDD UL/DL config 2
      HARQ process can be reduced e.g. 4 than max number.
For UE performance tests to use TDD config based on operators input
    Use 3DL 1UL for first round simulation alignment

## Slide 6
http://www.3gpp.org/ftp/TSG_RAN/WG4_Radio/TSGR4_87/Docs/R4-1806119.zip