## Slide 1
3GPP TSG-RAN WG4 #87 R4-1806190 Busan, KR, 21st – 25th May, 2018
Agenda item: 7.2.2.1.1 - [FR1] Band specific A-MPR -
Document for: Approval
n1 A-MPR for protecting PHS
KDDI Corporation

## Slide 2: Background
A-MPR discussion has been started for several bands.
For n1 in Japan, A-MPR for protecting PHS is necessary. Several contributions were submitted in RAN4#86-bis.
In this contribution, we show our view/analysis to specify n1 A-MPR for DFT-s-OFDM w./ SCS = 15kHz.

## Slide 3: Overview
KDDI has requested simulation cases below.
1920
1925
1930
1935
1940
15MHz
20MHz
Case#1:
Case#2:
Case#3:
Case#4:
Case#5:
Case#6:
10MHz
5MHz
15MHz
5MHz
MHz
Requirements for E-UTRA exist.
No E-UTRA requirements.
Requirements for Cat.M2 UE can be good reference model.
Requirements for E-UTRA exist.
No E-UTRA requirements.
Requirements for Cat.M2 UE can be good reference model.

## Slide 4: Assumption
In TS38.101, requirement for image is improved (up to 3dB) compared to those of TS36.101.
Hence, it is generally expected that emission level in NR will be lower than LTE for same output power cases.
3dB improvement would occur in maximum output power case.
RAN4 should also pay attention to the number of RBs which is increased for several CBWs. (106 for NR and 100 for LTE in 20MHz CBW, 15kHz SCS).

## Slide 5: Proposal#1
For Case#1 and Case#2 below, up to 10 dB A-MPR should be specified. This means 1 dB improvement from LTE era.
<Justification>
In LTE, 11dB A-MPR (12dBm transmission case) was specified based on 1RB transmission. So it would be impossible to enjoy 3dB improvement but a few improvement can be still expected.
1920
1925
1940
15MHz
20MHz
Case#1:
Case#2:
MHz
Requirements for E-UTRA exist.

## Slide 6: Proposal#2
For Case#5, up to 3dB A-MPR should be specified. For Case#6, A-MPR is not necessary for protecting PHS.
<Justification>
We referred A-MPR requirements for Cat.M2 Band 1 UE. In addition, image improvement is also taken in account (see more in detail analysis in the next slide).
20MHz
1920
1925
1940
Case#5:
Case#6:
MHz
1930
5MHz
5MHz
Requirements for Cat.M2 UE can be good reference model.
Requirements for Cat.M2 UE can be good reference model.

## Slide 7: Analysis of Proposal#2
GB (1MHz) | RB | RB | # 0 | # 1 | # 2 | # 3 | # 4 | # 5 | # 6 | # 7 | # 8 | # 9 | # 10 | # 11 | # 12 | # 13 | # 14 | # 15 | RB | RB | GB (1MHz)
↓ NB index ※ NB index = 6RB, 6RB x 16 = 96RB
100RB
20MHz
5MHz
1920 1925 1930 1940
Case#6:
In TS36.101, no A-MPR is required for NB index = 3, RBstart = 0, LCRB = 24. This is almost compatible with Case#6.
In addition, A-MPR requirements for Cat.M2 Band 1 UE were specified based on assumption of “Low cost PA” although this is not officially recorded. Hence, NR n1 UE should show better performance than that.

## Slide 8: Proposals
<For n1 15kHz SCS>
Proposal#1: A-MPR for protecting PHS should be up to 10 dB for Case#5 and Case#6.
Proposal#2: For Case#5, up to 3 dB A-MPR should apply. For Case#6, no A-MPR is necessary.

## Slide 9: FYI: Requirements for NS_05 from TS36.101
Channel Bandwidth [MHz] | Parameters |  |  |  |  |  |  |  |  |  |  | 
15 | Fc [MHz] | 1932.5 |  |  |  |  |  |  |  |  |  | 
 | RBstart | 0-7 | 8 – 66 |  |  |  |  |  | 67-74 |  |  | 
 | LCRB [RBs] | ≥1 | ≤30 |  | 31 – 54 |  | >54 |  | ≤6 |  | >6 | 
 | A-MPR [dB] | ≤11 | 0 |  | ≤3 |  | ≤5 |  | ≤5 |  | ≤1 | 
20 | Fc [MHz] | 1930 |  |  |  |  |  |  |  |  |  | 
 | RBstart | 0-23 | 24-75 |  |  |  |  |  |  | 76-99 |  | 
 | LCRB [RBs] | ≥1 | ≤24 | 25 – 40 |  | 41 – 50 |  | > 50 |  | ≤6 |  | >6
 | A-MPR [dB] | ≤11 | 0 | ≤3 |  | ≤5 |  | ≤10 |  | ≤5 |  | ≤1
Table 6.2.4-18: A-MPR for "NS_05"
BW [MHz] | 20 |  |  |  | 
Fc [MHz] | 1930 |  |  |  | 
(NBindex,RBstart) | (0,<6) | (0,<6) | (1,<6) | (2,<6) | (2,<6)
LCRB | 9, 12 | ≥15 | ≥15 | 18 | 24
A-MPR [dB] | ≤1 | ≤4 | ≤3 | ≤1 | ≤2
NOTE 1: NBindex is the narrowband index that is defined in 6.2.7 in [4]. The resource block assignment is defined within the narrowband as defined in 5.3.3.1.12 and 5.3.3.1.13 in [5]. |  |  |  |  | 
Table 6.2.4-18E: A-MPR requirements for "NS_05" for Cat-M2 power class 3 UE