## Slide 1: Way forward on network-based CRS IM
Huawei, HiSilicon, …
3GPP TSG-RAN WG4 Meeting #87 Busan, Korea, 21st – 25th May, 2018
Agenda item: 6.29
R4-1807379

## Slide 2: Background
The signalling support for network-based CRS interference mitigation includes:
  Information from the network to make the UE aware of whether network-based CRS interference mitigation is enabled or not:
    The following SI information is needed at least for UE in RRC_IDLE:
      Network-based CRS interference mitigation is enabled or disabled in the serving cell
      NOTE: This information should be provided to the UE as early as possible
    In RRC_CONNECTED, the dedicated RRC signaling (e.g., neighCellsCRS-Info and neighCellsCRS-InfoSCell in TS 36.331) is enhanced to include an indication whether the network-based CRS interference mitigation is enabled or not in the serving cell(s), including PSCell and SCells, and one or more neighbor cells
    In RRC_CONNECTED, the UE should be configured with CRS muting information for the target cell e.g. in handover command
RAN4 will specify applicable requirements for Rel-15 UEs capable of supporting network-based CRS interference mitigation and define the corresponding warm-up/cool-down subframes in TS 36.133 for RRC_IDLE and RRC_CONNECTED on dedicated carriers where CRS muting is used

## Slide 3: WF on Signalling Support
Baring information carried by system information is used to refrain legacy UEs from camping on the CRS mitigated cell.
CRS mitigation information carried by SIB is used to indicate the UEs about whether the CRS mitigation is enabled or not in the serving cell.
Neighbour cells with enabled CRS mitigation are excluded from the neighbour cell info list of intra-frequency in SIB4 and inter-frequency in SIB5 for legacy UE.
Network should be able to decide when the radio link condition is bad either for uplink or downlink, and keep full bandwidth CRS until radio link failure occurs or the radio link condition gets better.

## Slide 4: RAN4 Requirements
Scenario | Warm-up | Cool-down | Full BW CRS duration in addition to warm-up and cool-down
All configured paging occasions | [4] | [0] | All paging occasions
SI acquisition (SIB1 and SI-window) | [4] | [0] | All SI reading windows(incl. SIB1 and all other SIBs)
Prior to RA transmission occasions | [4] | [0] | In Connected mode from the start of RAR window to the completion of handover; In IDLE mode, from the start of RAR window to the completion of RRC configuration
Msg2 monitoring duration | [4] | [1] | 
Msg4 monitoring duration | [4] | [1] | 
On-duration of DRX | [4] | [4] | During DRX active time
SR over PRACH | [4] | [1] | From the start of RAR window to the reception of Msg. 2
SR over PUCCH | [4] | [1] | from the SR transmission to the UL grant
RSTD measurement | [4] | [0] | All OTDOA subframes