## Slide 1: Way forward on NR RRC requirements
Huawei, HiSilicon, …
3GPP TSG-RAN WG4 Meeting #87 Busan, Korea, 21st – 25th May, 2018
Agenda item: 7.10.2.1
R4-1807381

## Slide 2: Background
Ran4 Agreements in the previous LS R4-1706905
  If the multiple measurement objects refer to the same NR carrier frequency, the UE can measure the carrier frequency with a single measurement for some of measurement object configurations. In that case, aligned with reply to question 1 on RAN4 terminology, RAN4 view is that the separately configured measurement objects on the same carrier frequency can be counted as 1 frequency layer for some of measurement object configurations.
RAN2 #99bis Agreements
  Working assumption is confirmed (UE receives independent measurement configuration from MN and SN. UE does not do any manipulation of parameters in order to make the measurements configurations consistent (i.e. network is responsible to ensure they are consistent if it wants to ensure these are considered as a single measurement layer)

## Slide 3: Way forward
Capability-wise,
  Multiple identical MOs configured from MN and SN can be counted as 1.
  MOs with different numerologies cannot be counted as 1
  MOs with different SMTC configurations cannot be counted as 1
Since the MO is not used in the RAN4 spec, when the E-UTRA PCell and NR PSCell configure the same NR carrier frequency layer to be monitored, this layer shall be counted only once only if the UE can measure the carrier frequency with a single measurement
Considering multiple MOs that target the same frequency carrier,
  No additional UE requirements shall be defined for multiple MOs with different numerologies
  No additional UE requirements shall be defined for multiple MOs with different SMTC configurations
  UE measurement activities upon receiving multiple MOs are up to implementation