## Slide 1: Way forward on channel models for NR UE demodulation requirements
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #87
South Korea, Busan, 21 – 25 May 2018
Agenda Item: 6.18.1
R4-1808028

## Slide 2: FR1 Channel Models
RAN4 86bis agreements
  Use simplified TR 38.901 TDL channel models
    FFS for power delay profiles
    FFS for Delay spread values
    FFS how to simplify the models
    FFS MIMO antenna correlation models

## Slide 3: FR1 Channel Models
Channel model simplifications
  Simplify the existing 38.901 TDL channel models by choosing strongest paths
    Option 1: Choose strongest paths that contribute to [95%] of total power.
      Examples of simplified profiles for Option1 provided in the next slides
    Option 2: Choose [7] strongest paths that contribute for NLOS PDPs
    Apply normalization of the normalized DS after removing the weak paths (DS RMS = 1).
  Use equidistant delay modelling grid for TDL channel models after DS scaling with grid step ΔT ≤ 1/BW.
    BW = [200] MHz
    Paths that end up with the same delay will be combined into a single path by adding their respective powers
  Note: Initial simulations for July AH can be done based on non-simplified TDL models

## Slide 4: FR1 Channel Models
Channel model for initial simulations
  Model #1
    TDL-A
    DS = 30 ns
    Max Fd = 10 Hz
    Low antenna correlation
  Model #2
    TDL-C
    DS = 300 ns
    Max Fd = 100 Hz
    Low antenna correlation
  Note: This is only for initial simulation alignment. The example models are not for final channel model definition and parameters can be changed.

## Slide 5: FR1 Channel Models
Channel model for performance requirements are FFS
  Power delay profiles
    Option 1: TDL-A
    Option 2: TDL-B
    Option 3: TDL-C
    Option 4: TDL-D
    Option 5: TDL-E
  Delay spread values is FFS
    Option 1: 30 ns
    Option 2: 100 ns
    Option 3: 300 ns
  Doppler spread is FFS
  MIMO correlation models
    Use low antenna correlation for initial simulations
    Further discuss other antenna correlations models.

## Slide 6: Backup

## Slide 7: For Information: Simplified PDPs for Option 1

## Slide 8: For Information: Simplified PDPs for Option 1