## Slide 1: WF for Single UL EN-DC DC_(n)71B
T-Mobile, Ericsson, Nokia, Intel, Apple, Motorola Mobility
3GPP TSG-RAN WG4 Meeting #87 R4-1808117 Busan, Korea (Republic of), 21 - 25 May 2018

## Slide 2: WF
For DC_(n)71B, a Note 1 is inserted to 38.101-3 as shown below
Note I: For type 1 UE, Existing power limitation rules still apply including that in a situation when in an equal priority power situation the PDCCH link is given priority and includes dropping the non-PDCCH link. In the initial situation the LTE link will be configured with the PDCCH.
Note II: Type 1 UE supports dynamic power sharing. Type2 UE does not support dynamic power sharing.