## Slide 1: WF on FR1 HPUE behaviour
CMCC
3GPP TSG-RAN WG4 Meeting #87 R4-1808196
Busan, KR, 21th – 25th May, 2018

## Slide 2: Background
It was agreed in last meeting WF (R4-1806893) that:
  To solve the SAR issue for power class 2 UE, a UE capability of maxUplinkDutyCycle is proposed to be defined which represents the maximum percentage of uplink time that can be scheduled during [X]ms to ensure compliance with applicable electromagnetic energy absorption requirements.
    The default value of maxUplinkDutyCycle is 50%. E.g. If the field is absent, the UE shall apply the default value.
  For a power class 2 capable UE operating on Band n41 n77 n78 n79, when the percentage of uplink time scheduled by the network in [X]ms is larger than its capability, UE is allowed to do power back off and the requirements for power class 2 are not applicable, and the corresponding requirements for a power class 3 UE shall apply.
An LS was sent to inform RAN2 on the signaling impact (R4-1805786)
RAN4 continue to discuss and determine the value of evaluation period [X]ms in May meeting

## Slide 3: Way forward
The uplink transmission time is in terms of symbols
If the percentage of uplink symbols transmitted in a certain evaluation period is larger than maxUplinkDutyCycle as defined in TS 38.331, the requirements for power class 2 are not applicable, and the corresponding requirements for a power class 3 UE shall apply.
  The exact evaluation period is up to UE implementation, no less than one radio frame. Such functionality does not need to be tested.
  The default value of maxUplinkDutyCycle is 50%. E.g. If the field is absent, the UE shall apply the default value.
  These above requirements only apply to UE requirements specification, e.g. 38.101-1
  No additional constraints on BS scheduling but BS may consider maxUplinkDutyCycle
  Whether power class change due to the UL duty cycle exceeds UE capability will cause UL radio link failure problem is FFS

## Slide 4: Reference
[1] R4-1806256 TDD UL/DL configuration HPUE in FR1
[2] R4-1806818 More on HPUE behavior
[3] R4-1806890 Discussion on SAR evaluation period for NR HPUE