## Slide 1: WF on SCS restriction in BWP operation
Qualcomm Incorporated
3GPP TSG RAN WG4 Meeting #87 R4-808259 Busan, Korea, May 21st – 25th, 2018

## Slide 2: Background
In RAN4#AH-1801 [1] we agreed to the following
UE behavior
  The UE meets RF requirements related to it’s configured BWP according to UE CBW (no additional BWP related RF requirements)
    FFS whether UE CBW next highest value after BWP bandwidth
  How the UE configures it’s RF in order to operate the BWP and meet the CBW based RF requirements is implementation dependent
UE RF requirements
  Single BWP case: single CC RF requirements apply with UE CC BW
  Multiple BWPs case : intra-band CA RF requirements apply with UE CC BW
[1] R4-1801006, WF on wideband operation of NR UE, 3GPP TSG-RAN WG4 #AH-1801 Meeting, San Diego, California, USA, Jan. 22 – 26, 2018

## Slide 3: SCS Restriction in BWP operation
RF requirements
  Agreement: RF requirements are based on UE CC BW
  RAN2 signaling is configuring UE with multiple CC BW’s (per SCS)
    BWP switch may imply switching from one CC BW to another
      BWP switch may cause change in RF requirements that UE has to satisfy
  RAN4 had defined UE RF requirements based on UE CC BW such that BWP switch shouldn’t change RF requirements.
  Companies to investigate the implication of a UE configured with different UE CC BW’s on BWP switching

## Slide 4: SCS Restriction in BWP operation
Baseband capability
  Agreement: How the UE configures it’s RF in order to operate the BWP and meet the CBW based RF requirements is implementation dependent
  SCS of a BWP needs to be restricted so that the UE can always operate its RF in UE CC BW, irrespective of BWP BW.
    UE’s will have a baseband limitation in terms of FFT size
    SCS of a BWP should be such that UE operating in CC BW and BWP SCS is within its FFT size
  Two options to resolve this
    Option 1: SCS restriction needs to be across UE’s
    Option 2: Define a UE capability for UE’s that will not need this restriction.

## Slide 5: SSB Processing
SSB processing of data and SSB with different SCS depends on UE capability
  No SCS restriction needed in this case.
  If UE declares the capability to process SSB and data with different SCS
    UE needs to support all possible combinations of CC BW’s and SSB SCS.