## Slide 1: WF on MU and TT for receiver requirements
R4-1808366 Ericsson

## Slide 2: Combination of uncertainty factors at the receiver
Methodology:
(Root Square) subtract expected matching loss from conducted MUs for wanted and interfering signals
  This gives an expected MU for the test equipment and other conducted components for everything except the matching MUcond_wanted -match and MUcond_int-match
(Root Square) subtract test equipment and matching uncertainty from the EIS MU
  This in effect gives a combined uncertainty budget for the OTA chamber MUchamber-match
Agree a figure for miss match (can be same as existing OTA value) MUmatch
Root sum square combine the two uncertainty values from step (1) and the OTA uncertainty from step 2
  This sum only counts the OTA uncertainty and matching uncertainty once
Add the ACLR effect (MUACLR)to the result of the root sum square in (4)
((MUcond_wanted –match2 + MUcond_int-match2 + MUchamber-match2 + MUmatch2 )^0.5) + MUACLR

## Slide 3: Combination of uncertainty factors at the receiver
In mathematics:
i.e.

## Slide 4: Some values:
Example: Blocking, below 3GHz
= 0.2 dB --- example
  Companies should provide views on mismatch uncertainty by the July ad-hoc

## Slide 5: Need for PA
For the July Ad-Hoc, companies are encouraged to provide information on:
  Expected TX power for OTA testing for each RX requirement considering chamber type and operating frequency
  View as to whether a PA is needed in the test setup for each requirement
  Where a PA is needed:
    The PA output power
    Expected PA ACLR performance
    Expected uncertainty in PA output power level
The information provided to the July ad-hoc will be used to make decisions on:
  Which requirements necessitate PA in the test setup
  Impact of the PA on measurement uncertainty and ACLR effect