## Slide 1: 3GPP TSG-RAN WG4 Meeting #87 Busan, Korea (Republic of), May 21 – 25, 2018
Qualcomm, Ericsson, Huawei
Way forward on sTTI UE demodulation and CSI requirements
R4-1808475

## Slide 2: SPDCCH and Slot/Subslot-PDSCH demodulation requirements
Consider EVA30 for CRS-based sPDCCH and sPDSCH performance requirements.
Consider dual layer for DMRS-based sPDSCH performance requirements.
Companies are encouraged to provide the simulation results of sPDCCH and Slot/Subslot-PDSCH based on the agreement
Simulation assumption: R4-1805493

## Slide 3: Open issues for Subslot-based PDSCH
For sPDSCH performance requirements, companies to think about TE’s behavior in the case of retransmission to minimize the huge coding rate difference between the first transmission and retransmission.
  In case retransmission can happen on a subslot with significant difference in coding rate with first transmission, companies are encouraged to study the options:
    Option 1: DTX subslot index 3.
    Other options are not precluded.

## Slide 4: CQI reporting requirements
Consider wideband sPDSCH scheduling with PUSCH 1-1 with EPA5 channel for CQI reporting performance requirement with both CRS-based TM4 and DRMS-based TM9 sPDSCH.
Compute CQI2MCS mapping table based on slot/subslot index.
Companies are encouraged to provide:
  CQI2MCS mapping table
  Simulation results of CQI reporting
  Proposal of test points
Simulation assumption: R4-1805493

## Slide 5: FRC table for slot-based CRS-based PDSCH (For information)
Sub-frame | Slot index | Information bit payload per slot (for dual layer) | Binary channel bits per slot (for dual layer)
1,2,3,4,6,7,8,9 | 0 | 11448 | 22400
 | 1 | 14112 | 28288
0 | 0 | 9912 | 21248
 | 1 | 12576 | 26368
The following FRC table is based on 16QAM modulation and target coding rate ½

## Slide 6: FRC table for subslot-based CRS-based PDSCH (For information)
The following FRC table is based on 16QAM modulation and target coding rate ½
  MCS 16 has been considered for subslot index 1 and subslot index 5 to keep the same modulation order and closet possible coding rate to other subslots.

## Slide 7: FRC table for subslot-based CRS-based PDSCH (For information)
Sub-frame | Subslot index | Information bit payload per subslot (for dual layer) | Binary channel bits per subslot (for dual layer)
1,2,3,4,6,7,8,9 | 1 | 5160 | 12032
 | 2 | 4264 | 8832
 | 3 | 2984 | 5888
 | 4 | 4264 | 8832
 | 5 | 5160 | 12288
0 | 1 | 5160 | 12032
 | 2 | 3880 | 7680
 | 3 | 2664 | 5120
 | 4 | 3880 | 7680
 | 5 | 5160 | 12288