## Slide 1: Way forward on demodulation and CSI requirements for high capacity stationary wireless link and 1024QAM
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #87 R4-1807966
Busan, Korea (Republic of), May 21 – 25, 2018
Agenda Item: 6.21.4

## Slide 2: Demodulation requirements under fading conditions
Parameters | Value
Bandwidth | 10MHz
Channel model | EPA5
CFI (OFDM symbol for control channel) | 1
Duplex mode | FDD
Table 1: common parameters
For 1024QAM demodulation requirements, the test cases given in Table 2 with the common parameters given in Table 1 are identified

## Slide 3: Demodulation requirements under fading conditions
Table 2: Test cases for demodulation tests under fading conditions
No. | TM | PMI feedback (pre-coding) | MIMO layer | MCS | Antenna config.
1 | TM4 | Wideband PMI Feedback (PUSCH 3-1, Reporting interval =1) | 1-layer | MCS#23 (with 52752 bits) | 4x2 Low
2 | TM4 | Wideband PMI feedback (PUSCH 3-1, Reporting interval =1) | 2-layer | MCS#23 (with 52752 bits) | 4x4 Low
3 | TM9 | Option 1: Wideband PMI Feedback Option 2: Per-PRG Random Precoder | 1-layer | MCS#23 (with 52752 bits) | 4x2 Low
4 | TM9 | Option 1: Wideband PMI Feedback Option 2: Per-PRG Random Precoder | 2-layer | MCS#23 (with 52752 bits) | 4x4 Low
For 1024QAM demodulation requirements, the candidate test cases given in Table 2 with the common parameters given in Table 1 are identified
Test cases for demodulation fading tests for 1024QAM
  Tx EVM: 2%
FFS for applicability rule

## Slide 4: SDR test
Test parameters:
Transmission mode: TM3
Bandwidth: 10MHz
Antenna configuration: 2 x 2 for 2-layer transmission per CC, and 4 x 4 for 4-layer transmission per CC
MCS [TBD] for 2 x 2 2-layer transmission per CC, and MCS [TBD] for 4 x 4 4-layer transmission per CC
CFI = 1
Tx EVM: 2%

## Slide 5: CQI reporting test
Definition test:
Minimum requirement PUCCH 1-0 (Cell-Specific Reference Symbols): CRS based TM single codeword with TM1 under static channel in Annex B.1
  Bandwidth:
    FDD: 10MHz
    TDD: 20MHz

## Slide 6: DMRS overhead reduction
Further alignment of simulation results
DMRS ports 7,8,11,13 with OCC=4
16QAM, EPA5, 4-layer
TBD FRC test case number