## Slide 1: WF on measurement gaps for dense PRS
Ericsson
3GPP TSG-RAN WG4 Meeting #87 R4-1808008
Busan, Republic of Korea, 21st – 25th May 2018
Agenda Item: 6.20.4.4

## Slide 2: Requirements impact
RSTD measurement period:
  The existing UE Cat M1 and Cat M2 measurement period requirements (generically formulated with respect to MGL and MGRP) for RSTD measurements in gaps shall also apply with the new gaps
RLM requirements:
  When the UE is configured with new measurement gaps for RSTD measurements, the UE shall also perform RLM. If there is no overlap between the new measurement gaps and configured MPDCCH subframes for UE monitoring, the UE shall meet the existing requirements; otherwise, the out-of-sync and in-sync evaluation periods can be longer than currently defined in 36.133
RRM requirements:
  RRM cell identification delay and measurement delay may be longer while the UE is using a new measurement gap pattern configured for RSTD measurements

## Slide 3: New measurement gap patterns
Gap Pattern Id | MGL (ms) | MGRP (ms) | Applicability
rstd0 | 10 | 80 | Not any measurement gap pattern among rstd0-rstd20 can be be configured for a UE in different conditions, including whether the UE is configured with a single or multiple PRS configurations in a cell Details of applicability rules are TBD.
rstd1 | 10 | 160 | 
rstd2 | 10 | 320 | 
rstd3 | 10 | 640 | 
rstd4 | 10 | 1280 | 
rstd5 | 14 | 160 | 
rstd6 | 14 | 320 | 
rstd7 | 14 | 640 | 
rstd8 | 14 | 1280 | 
rstd9 | 24 | 320 | 
rstd10 | 24 | 640 | 
rstd11 | 24 | 1280 | 
rstd12 | 32 | 320 | 
rstd13 | 32 | 640 | 
rstd14 | 32 | 1280 | 
rstd15 | 54 | 640 | 
rstd16 | 54 | 1280 | 
rstd17 | 64 | 640 | 
rstd18 | 64 | 1280 | 
rstd19 | 80 | 640 | 
rstd20 | 80 | 1280 | 
NOTE 1: Measurement gap patterns rstd0─rstd20 can only be configured for RSTD measurements requiring such gaps and used during the RSTD measurement period corresponding to these measurements. |  |  |