## Slide 1: WF on 2RX Requirements for vehicle mounted NR UE at FR1
LG Electronics, Volkswagens, General Motors, Samsung, Qualcomm Incorporated, Harman, OPPO
3GPP TSG-RAN WG4 #87 Meeting Busan, Korea, 21 - 25 May 2018 Agenda Item: 7.5.9
R4-1808159

## Slide 2: Background
In LS from 5GAA, Car OEM requested to allow 2Rx antenna as exceptional case for vehicle mounted NR UE at frequency bands where 4Rx is mandated.
  Use case is infotainment or e-call service using Uu interface
  4Rx mandating for some NR operating bands (n7, n38, n41, n77, n78, n79) at FR1 will restrict the design freedom of Car OEM.
  If exceptional 2Rx antenna is not agreed, slower deployment of vehicle mounted NR UE is expected which can result in less positive market perception of 5G.
  This exception request is not for the NR V2X service specified in SA1 in Rel-15.
    No NR V2X WI in RAN as of now.
    This issue is irrelevant with NR V2X.

## Slide 3: Issues
Issues
  1 : Coverage issues with 4Rx Handheld device and 2Rx Vehicle UE (Huawei, CMCC, Vodafone)
    Link budget and SNR for the receiver
  2 : Need to distinguish Handheld UE and Vehicle UE in FR1? (Qualcomm, Skyworks, Vodafone)
    Need to declare its type to TE vender?
  3 : Demodulation / RRM impact with 2Rx vehicles (Intel, Ericsson)
  4: Justification from automotive industry about the difficulty of mounting 4Rx antennae on the roof of the vehicle (Huawei, Vodafone, CMCC)

## Slide 4: WF
2Rx vehicle NR UE with Uu interface will be targeted to be in Rel-15
  Related CR and LS to 5GAA should be further discussed and concluded at RAN #80 (June 2018)
As technical aspect, RAN4 will endorse the related CR [3] when all issues are addressed in RAN4 #87 meeting.
  RAN4 send LS on the RAN4 status to RAN
If RAN4 have remaining issues in RAN4 #87 meeting, those will be addressed in RAN #80.

## Slide 5: Appendix
Issues
  1 : Coverage issues with 4Rx Handheld device and 2Rx Vehicle UE
  2 : Need to distinguish Handheld UE and Vehicle UE in FR1?
  3 : Demodulation / RRM impact with 2Rx vehicles
  4 : The difficulty of mounting 4Rx antennae on the roof of the vehicle
Answers
  Answers for issue 1:
    Antenna gain [3] in Car is much higher than handheld
    DL: Taking antenna gain into account, Car with 2Rx have no less SNR than handheld device with 4Rx UE
    UL: Taking antenna gain into account, Car has superior performance than handheld device.
  Answers for issue 2:
    UE declare its type for testing
      For RFIC GCF test, both 2Rx and 4Rx can be declared for all chipset
      For device GCF test, handheld device can only declare 4Rx
  Answers for issue 3 :
    Demodulation/RRM with requirements applied per number of declared Rx.

## Slide 6: Answer for issue 4:
Provisions to support integrated 4 antennas inside a smartphone is very different from that of automotive. Implementation difficulties include:
  Multiple radios
  Antenna connector availability
  Additional antenna cables
  Space reserved for communication modules
  RF compensator requirements to compensate loss
  Additional heat compensation requirements (ambient/operating temperature until 95°C)
    The 5G device inside automotive must be fully functional, heat sink measures could be required when antenna chains increase within telematics control unit
  Costs associated with points 1-6 is significant for automotive development. Cannot be considered trivial.
Mandating 4 RX impose serious constraints to support 5G compatible device in automotive sector.
Working group level agreements in RAN 4 #87 will avoid the risk of automotive industry delaying adoption of 5G Sub-6 GHz technology and will enable to further enhance automotive vertical integration in 3GPP scope.
The technology definition is recommended to be adaptive and flexible, when supportive technical and business related facts exist.

## Slide 7: References
[1] R4-1806681 Consideration on 2Rx REFSNES for NR vehicular UE at FR1 [2] R4-1806682 Draft CR on REFSENS requirements for NR vehicular UE at FR1
[3] ECCREP228 (Refer Antenna gain in 2.4)
[4] http://5gaa.org/membership/our-members/
[5] LS from 5GAA to 3GPP RAN 4
[6] 3GPP TS 36.101 Chapter 7 on RX REFSENS