## Slide 1: 3GPP TSG RAN WG4 Meeting #87 R4-1808198 Busan, Korea, May 21st – 25th, 2018
WF on spherical coverage requirement on FR2
Qualcomm Incorporated, Verizon, Telstra, NTT Docomo, CMCC, Vodafone, Orange, Telecom Italia, Motorola Mobility, Nokia, Nokia Shanghai Bell, China Telecom, China Unicom, BT plc., Ericsson, Dish Networks, SKT, KT, Softbank, Deutsche Telekom, Interdigital, T-Mobile USA, NXP, US Cellular, Panasonic, SGS Wireless, Bureau Veritas, Sharp, Mitsubishi Electric

## Slide 2: Background
The impact of spherical coverage on the network performance shows that better spherical coverage leads to better system performance and network coverage as shown in R4-1807658

## Slide 3: Way forward on spherical coverage requirements
24-28GHz bands
  50%-ile cdf of spherical coverage requirement for EIRP for handheld UE is defined as 12.5dBm (9.9dB lower than peak EIRP)
  50%-ile cdf of spherical coverage requirement for EIS for handheld UE is defined as -78.4dBm for 50MHz SC QPSK 1/3 (9.9dB higher than EIS)
39GHz bands
  50%-ile cdf of spherical coverage requirement for EIRP for handheld UE is defined as 8.5dBm (12.1dB lower than peak EIRP)
  50%-ile cdf of spherical coverage requirement for EIS for handheld UE for GHz is defined -73.6dBm for 50MHz SC QPSK 1/3 (12.1dB higher than peak EIS)