## Slide 1: WF on NR BS out-of-band blocking measurement step size
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN WG4 Meeting#87
Busan, Korea, 21 – 25 May 2018
Agenda Item: 7.8.4.1
R4-1808330

## Slide 2: Background
Contributions on NR BS out-of-band blocking measurement step size have been discussed in RAN4:
  [1] R4-1800027, “TP to TR 38.817-02: NR BS out-of-band blocking step size for FR1 (7.5.1, 10.6)”, Nokia, Nokia Shanghai Bell.
  [2] R4-1800028, “TP to TR 38.817-02: NR BS out-of-band blocking requirements for FR2 (10.6)”, Nokia, Nokia Shanghai Bell.
  [3] R4-1802740, “TP to TR 38.817-02: NR BS out-of-band blocking requirements for FR2 (10.6)”, Nokia, Nokia Shanghai Bell.
  [4] R4-1804248, “TP to TR 38.817-02: NR BS out-of-band blocking requirements for FR2 (10.6)”, Nokia, Nokia Shanghai Bell.
  [5] R4-1804498, “On OTA OOB RX blocking requirement for FR2”, Ericsson.
  [6] R4-1806601, “TP to TR 38.817-02: NR BS out-of-band blocking requirements for FR2 (10.6)”, Nokia, Nokia Shanghai Bell.

## Slide 3: Way forward on BS type 2-O
Objective: To reduce the amount of time used for unnecessary measurement especially for the time consuming OTA conformance testing, while continue to ensure that any spurious response falls within the receive bandwidth will still be limited so that the receiver filter selectivity is verified with sufficient granularity.
Agreement: The measurement step size of the NR BS type 2-O OTA out-of-band blocking conformance testing for interfering signal at frequency above 6 GHz should be set as follows:
BS Channel bandwidth of wanted signal [MHz] | 50 | 100 | 200 | 400
Measurement step size for interfering signal [MHz] | 15 | 30 | 60 | 130