## Slide 1: Way forward on Beam management requirements in NR
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #87 Busan, Korea, 21st – 25th May, 2018
Agenda item: 7.10.4.4
R4-1808444

## Slide 2: Agreements on Beam failure detection
The requirements on both CSI-RS based beam failure detection and SSB based beam failure detection will be introduced, and the following aspects will be specified:
  BLER value for the threshold Qout_LR.
  Maximum number of beam failure detection RS resources, which is defined as 2.
  Hypothetic PDCCH parameters for beam failure instance
    Reuse the parameters for RLM out-of-sync without power boosting for PDCCH/PDCCH-DMRS, which means that the corresponding SINR level of Qout_LR will be 4dB higher than the corresponding SINR level of Qout and slightly lower than the corresponding SINR level of Qin .
  L1 indication interval of two successive beam failure instance, which can be defined as the maximum values between the shortest periodicity of BFD-RS resources and 2ms
  L1 evaluation period for beam failure instance evaluation
    Reuse the requirements for RLM in-sync evaluation, since the corresponding SINR level of Qout_LR and Qin are quite close.
    Low boundary is not applied for BFD evaluation period, since the low boundary for L1 indication interval is defined as 2ms and will be always shorter than the shortest periodicity of BFD RS resource (i.e. 5ms)
      When CSI-RS
    The conditions on Rx beam sweeping operation for RLM are reused for beam failure detection.

## Slide 3: Agreements on Candidate Beam detection
The requirements on both CSI-RS based candidate beam detection and SSB based candidate beam detection will be introduced, and the following aspects will be specified:
  The L1-RSRP measurement period for each configured RS resource in set q1, which will be specified in core requirements.
    FFS how many samples are assumed.
    FFS whether to reflect Rx beam sweeping in FR2
  The measurement accuracy of L1-RSRP for candidate beam detection will be studied in performance part.
  Requirements on accuracy and its side condition for L1-RSRP should be specified as a package.
  FFS whether to use the same L1-RSRP accuracy requirements of for both candidate beam detection and beam reporting.

## Slide 4: Agreements on Beam Reporting
  Both CSI-RS based and SSB based L1-RSRP measurement period for beam reporting will be specified.
    FFS how to capture the requirements
  The measurement accuracy of L1-RSRP for beam reporting will be studied in performance part.
  It is FFS, for beam reporting, the requirements on L1-RSRP measurement accuracy can be based on single-shot or multi-shot measurement.
  Requirements on accuracy and its side condition for L1-RSRP should be specified as a package.
  FFS whether to use the same L1-RSRP accuracy requirements of for both candidate beam detection and beam reporting.