## Slide 1: WF on the clarification of NR BS TAE applicable scenarios
NTT DOCOMO, INC.
R4-1808486
3GPP TSG-RAN WG4 Meeting #87
Busan, Korea, 21 - 25 May, 2018
Agenda 7.7.2.4.2.3

## Slide 2: Background
In RAN4 #86bis, following contribution triggers the discussion of understanding regarding TAE requirements for MIMO or TX diversity, and intra-band C CA.
  R4-1805339 NR BS TAE for distributed MIMO deployment scenarios NTT DOCOMO, INC.
In RAN4 #86bis, following WF was agreed.
  R4-1805804 WF on NR BS TAE for inter-BS NTT DOCOMO, INC.
In RAN4 #87, this issue is further discussed based on following contributions.
  R4-1807576 NR BS TAE for inter-BS cases, NTT DOCOMO, INC
  R4-1806400 Discussion on scenario for BS TAE, Samsung
  R4-1807878 On NR BS TAE requirement for inter-BS, Nokia, Nokia Shanghai Bell
  R4-1807190 NR BS TAE for inter-BS scenario, NEC
  R4-1807182 Input to WF on NR BS TAE for inter-BS for MIMO, TX diversity and continuous CA, Ericsson LM R4-1807183 Input to WF on NR BS TAE for inter-BS with respect to inter-band CA and non-contiguous CA, Ericsson LMBackground can be found in above document.

## Slide 3: Background
When connecting 2 or more RRHs to 1BBU, the required TAE value between connectors inside each RRHs is not clear.
According to current specification (TS 38.104), the required TAE value for MIMO is specified as 65ns.
However, in distributed MIMO case (Figure 1), it is difficult to achieve 65ns TAE.
This document clarify the applicability of current TAE requirement
Figure 1. Example, Distributed MIMO case.
Required TAE value is not clear 65ns??

## Slide 4: Agreements
Applicability of TAE
  Existing TAE requirement for MIMO or Tx diversity, intra-band contiguous CA is applied for intra-BS
  Existing TAE requirement for intra-band non-contiguous CA and inter-band CA is applied for intra-BS and inter-BS
  Inter-BS TAE requirements for MIMO or Tx diversity, intra-band contiguous CA will be discussed in Rel-16.
The definition of “intra-BS”
  Intra-BS: Intra-site and co-location scenario
Configurations | TAE requirement | 
 | Intra-BS | Inter-BS
MIMO or Tx div. | 65ns | FFS in Rel-16
intra-band C CA | 260ns (FR1), 130ns (FR2) | 
intra-band NC CA | 3us | 3us
inter-band CA | 3us | 3us