## Slide 1
3GPP LTE Bands 46A-46D Combination
CableLabs, Broadcom, Charter Communications, Blackberry
05/24/2018
3GPP TSG-RAN4 Meeting #87
Busan, South Korea, 21-25 May 2018
R4-1808489

## Slide 2: Background 1: Channel bonding
1: See S2-183026
The figure shows the Wi-Fi 802.11ac channel structure used in 5 GHz .
This arrangement ensures that concurrent transmissions of the same bandwidth from two Wi-Fi nodes are either completely overlapping or completely disjoint. Also all co-channel nodes get similar priority to access their primary/secondary channels.
The same channel bonding rule is required for any technology using Wi-Fi like channel access scheme by
section 4.2.7.3.2.3 of ETSI EN 301 893.
LAA DL Type B channel access and LAA UL channel access use Wi-Fi like channel access scheme
LAA UL channel access already implements Wi-Fi channel bonding rules.

## Slide 3: Background 2: DL Type A and B Access
Section 15.1.5.1 of TS 36.213 specifies LAA DL multicarrier channel access rules.
Type A channel access involves independent CAT4 LBT on all carriers.
Type B channel access is Wi-Fi like channel access where CAT4 LBT is performed only on one carrier and 25 us LBT is performed on all other carriers
  This type of channel access requires Wi-Fi like channel bonding per ETSI regulations as well as LAA Wi-Fi fair coexistence considerations.

## Slide 4: Requirement from TS 36.300 (RAN 2)
Section 5.7 of 36.300 (v15.0) specifies:
“If the absence of IEEE802.11n/11ac devices sharing the carrier cannot be guaranteed on a long term basis (e.g., by level of regulation), and for this release if the maximum number of unlicensed channels that E-UTRAN can simultaneously transmit on is equal to or less than 4, the maximum frequency separation between any two carrier centre frequencies on which LAA SCell transmissions are performed should be less than or equal to 62MHz.”
The above implies that L2 functionalities (for example, RRC SCell addition or MAC layer) will be disabled for band combinations of type 46A-46D if the above condition is not satisfied.
Thus, restrictions are imposed on both Type A and Type B channel access operation for LAA DL.
However, these restrictions could be removed for Type A channel access in LAA DL so that there is no restriction on carrier frequency separation (for Type A) channel access. Only Type B channel access in LAA DL requires restrictions.
A suggested way forward is to remove these restrictions from 36.300 (on both Type A and B) and to capture the channel bonding requirement for LAA DL Type B channel access along with the channel bonding requirement for LAA UL channel access in 5.7.4 of 36.104

## Slide 5: Suggested Modifications for 36.104
5.7.4 EARFCN sets for uplink and downlink transmissions on multiple Scells configured in Band 46
On a configured set of carriers with carrier frequencies that are a subset of any of the following sets of EARFCN, if the eNB schedules a UE to transmit in a subframe on the configured set of carriers, and if the UL grants scheduling PUSCH transmissions on any of the said set of carriers indicate Type 1 channel access procedure, and if the same ‘PUSCH starting position’ is indicated for all carriers, transmissions in accordance with the conditions for Type 2 channel access specified in clause 15.2.1 of [11] are allowed:
- for sets of two Scells: {47090, 47290}, {47490, 47690}, {47890, 48090}, {48290, 48490}, {50290, 50490}, {50690, 50890}, {51090, 51290}, {51490, 51690}, {51890, 52090}
- for sets of four Scells: {47090, 47290, 47490, 47690}, {47890, 48090, 48290, 48490}, {50290, 50490, 50690, 50890}, {51090, 51290, 51490, 51690}
[for sets of eight Scells: {47090, 47290, 47490, 47690, 47890, 48090, 48290, 48490}, {50290, 50490, 50690, 50890, 51090, 51290, 51490, 51690}]
On a configured set of carriers with carrier frequencies that are a subset of any of the following sets of EARFCN, downlink transmissions in accordance with Type B multi-carrier access procedure as defined in 15.1.5.2 of [11] are allowed:
- for sets of two Scells: {47090, 47290}, {47490, 47690}, {47890, 48090}, {48290, 48490}, {50290, 50490}, {50690, 50890}, {51090, 51290}, {51490, 51690}, {51890, 52090}
- for sets of four Scells: {47090, 47290, 47490, 47690}, {47890, 48090, 48290, 48490}, {50290, 50490, 50690, 50890}, {51090, 51290, 51490, 51690}
[for sets of eight Scells: {47090, 47290, 47490, 47690, 47890, 48090, 48290, 48490}, {50290, 50490, 50690, 50890, 51090, 51290, 51490, 51690}]

## Slide 6: Suggested Modification for 36.300
Modify 36.300 section 5.7 as follows:
Carrier aggregation with at least one SCell operating in the unlicensed spectrum is referred to as Licensed-Assisted Access (LAA). In LAA, the configured set of serving cells for a UE therefore always includes at least one SCell operating in the unlicensed spectrum according to Frame structure Type 3, also called LAA SCell. Unless otherwise specified, LAA SCells act as regular SCells.
If the absence of IEEE802.11n/11ac devices sharing the carrier cannot be guaranteed on a long term basis (e.g., by level of regulation), and for this release if the maximum number of unlicensed channels that E-UTRAN can simultaneously transmit on is equal to or less than 4, the maximum frequency separation between any two carrier center frequencies on which LAA SCell transmissions are performed should be less than or equal to 62MHz. The UE is required to support frequency separation in accordance with TS 36.133 [21].
LAA eNB and UE apply Listen-Before-Talk (LBT) before performing a transmission on LAA SCell. When LBT is applied, the transmitter listens to/senses the channel to determine whether the channel is free or busy. If the channel is determined to be free, the transmitter may perform the transmission; otherwise, it does not perform the transmission. If an LAA eNB uses channel access signals of other technologies for the purpose of LAA channel access, it shall continue to meet the LAA maximum energy detection threshold requirement.

## Slide 7: Conclusions
By adopting the suggested modifications, LAA DL multicarrier operation for band combination 46A-46D is enabled for Type A DL channel access without any restrictions.
RAN4 would need to work in-sync with RAN 1 and 2 to properly update the LAA LTE CA specs.
To inform RAN1/RAN2 of the decision, RAN4 can send an LS to both groups.
For any clarification on the meaning of “If the absence of IEEE802.11n/11ac devices sharing the carrier cannot be guaranteed on a long term basis (e.g., by level of regulation)”, RAN4 can request a response from RAN1 through an LS.

## Slide 8: Appendix

## Slide 9: CA 46A-46D Combination (TS36.101)
TS36.101 Rev 15. Table 5.6 1-3 (excerpt)
Notes:
46A and 46D is a non-contiguous CA combination.
It is not supported actually by 36.300 and 36.104.
Comments:
The LAA LTE DL and UL CA are paired.

## Slide 10: A and D Prefixes (TS36.101)
The 46A and 46D combination is a non-contiguous combination employing 1x20 MHz (Band 46A) and
3x20MHz (Band 46D).

## Slide 11: 36.104 UL Scells

## Slide 12
Background: TS36.213