## Slide 1: Way forward on the study scope of RF co-existence of LTE MTC and NB-IoT with NR
Ericsson, […..]
R4-1810078

## Slide 2: Background
In RAN plenary #78, a way forward on the study of RF co-existence of LTE MTC and NB-IoT with NR was approved [1].
The objective of the way forward is summarized as following:
  In August meeting, RAN4 is tasked to discuss the scope for the study of LTE MTC and NB-IoT RF coexistence with NR
    With limited number of TU allocated
  Come back to RAN#81 with the stable scope for a Rel-16 SI or WI.
In [2] and [3], the scope and study areas for RF co-existence of LTE-MTC and NB-IoT with NR was investigated and study areas proposed.
References:
[1] RP-181437, “Way forward on the study of RF co-existence of LTE MTC and NB-IoT with NR”
[2] R4-1810077, “On NB-IoT RF co-existence with NR”, Ericsson
[3] R4-1810496, “On LTE MTC RF co-existence with NR”, Ericsson

## Slide 3: Way forward
The scope and study areas for SI on RF co-existence of LTE MTC and NB-IoT with NR should be as following:
  For NB-IoT:
    To early verify NB-IoT in-band and guard band coexistence with NR FDD and 15 kHz SCS:
      Channel raster alignment between NB-IoT and NR for all concerned bands.
      Study on NR spectrum utilization and implications for further reduced the guard with NB-IoT operating in guard band. The study should outline feasible combinations without RF backward compatibility impact.
    In addition to previous areas, to early verify NB-IoT in-band and guard band coexistence with NR TDD and 15 kHz SCS:
      Synchronization between NR, LTE and NB-IoT for unpaired bands.
      Further channel raster alignment investigation if needed.
    And to finalize NB-IoT with NR coexistence study, in addition to previous areas:
      RF-coexistence study between NB-IoT and NR for 30 kHz SCS when efficient deployment is outlined (60 kHz should be done later).
      Study the applicable set of requirements when introducing NB-IoT, considering the need of adding NB-IoT in AAS specification in a separate WI.

## Slide 4: Way forward
  For LTE MTC
    Prioritize the deployment scenario of inband LTE-M service within a NR BS for the co-existing NR and LTE-M service with below considerations:
      Assume the fully awareness between the NR and LTE-M
      Prioritize the same subcarrier spacing 15kHz with LTE-M and NR
      Consider different channel raster and bandwidth options between LTE-M and NR for specific band, e.g n41
      Identify synchronization issue between LTE-M and NR for TDD band.
      Study the number of uplink guard subcarriers needed between LTE-M and NR to alleviate inter-subcarrier interference in the TDD bands.