## Slide 1: 3GPP TSG-RAN WG4 Meeting #88 Gothenburg, Sweden, 20 - 24 Aug 2018
Huawei, HiSilicon, …
Way forward on 8Rx demodulation and CSI tests
R4-1811384

## Slide 2: Applicability rules for 2Rx and 4Rx test cases for 8Rx capable UEs - Demodulation
Single carrier cases for 8Rx capable UEs :
Scenario1: All test cases specified in 8.2 to 8.8 with 2Rx are tested on any of the 2Rx supported RF band by connecting 2 out of the 8Rx with data source from system simulator, and the other 6 Rx are connected with zero input, depending on UE’s declaration and AP configuration. Same requirements specified with 2Rx should be applied.
Scenario2: All test cases specified in 8.10 with 4Rx are tested on any of the 4Rx supported RF bands by connecting 4 out of 8 Rx with data source from system simulator, and the other 4 Rx are connected with zero input, depending on UE’s declaration and AP configuration. Same requirements specified with 4Rx should be applied
Scenario3: For 8Rx capable UEs without any 2Rx supported RF but with 4Rx supported RF bands, all single carrier tests specified in 8.2 to 8.8 with 2Rx are tested on
  Option 1: Any of the 4Rx supported RF bands by duplicating the fading channel from each Tx antenna and add independent noise for each Rx antenna as 2x2 or 4x2
  Option 2: Any of the 8Rx supported RF bands by duplicating the fading channel from each Tx antenna and add independent noise for each Rx antenna as 2x2 or 4x2
Scenario4: For 8Rx capable e UEs without any 4Rx supported RF bands but with 2Rx supported RF bands, all single carrier tests specified in 8.10 with 4Rx tested on any of the 8Rx supported RF bands by duplicating the fading channel from each Tx antenna and add independent noise for each Rx antenna as 2x4 or 4x4.
Scenario5: For 8Rx capable UEs without any 2Rx supported RF and without 4Rx supported RF bands, all single carrier tests specified in 8.2 to 8.8 with 2Rx and 8.10 with 4Rx are tested on any of the 8Rx supported RF bands by duplicating the fading channel from each Tx antenna and add independent noise for each Rx antenna as 2x2 or 4x2 for 2Rx tests and 2x4 or 4x4 for 4Rx tests.
When tested on the 8Rx supported RF bands, SNR requirement is tightened by [3.0]dB and [1.5]dB for the legacy 2Rx and 4Rx test cases, respectively.

## Slide 3: Advance receiver test
For 8Rx capable UE without any 2Rx (or 4Rx) supported RF bands, the test cases regarding 2Rx (or 4Rx) requirement for the advanced receiver type A/B/C , ABS, and CRS assistance information can be skipped.
FFS the detailed set of test cases to skip for the above advanced receive types.

## Slide 4: Control channel demodulation performance tests
8Rx-capable UEs are not mandated to use 8Rx for the demodulation of the broadcast/control channels including PDCCH/PCFICH/PHICH/PBCH/ePDCCH
For cases conducted on 8Rx supported RF bands: the SNR requirement should remain the same as 4Rx UE

## Slide 5: UE declaration of AP configuration for control channels
For any demodulation tests including both PDSCH and PDCCH and CSI tests conducted in the 8Rx supported RF band, four receive antenna ports that UE may use for control channel demodulation are clarified via UE declaration
  When testing 2Rx/4Rx requirement in the 8Rx supported RF band, fading duplication and antenna mapping should ensure that the NT x 4 subchannel consisting of the UE-declared four receive antenna ports has the same diversity gain as the NT x 2 or NT x 4 channel of the original 2Rx/4Rx test.

## Slide 6: PDSCH demodulation performance tests
  Introduce 8Rx demodulation test(s)
    TM9
    Rank higher than four, including at least one rank from {6, 8}
    16QAM
    EPA5

## Slide 7: SDR tests
  64QAM
    Rank: 8
    Tx EVM: 6%
    Choose MCS from range [20-27]
  256QAM
    Rank:
      Option 1: Rank 6 if rank 8 is not feasible considering the working point of 27dB for 256QAM
      Option 2: Rank 8
    Tx EVM: 3%
    Option 1: Choose MCS from range MCS [20-22]
    Other options are not precluded
  Rank 2/4 SDR tests
    FFS applicability rule

## Slide 8: CSI tests
CQI reporting definition under AWGN
  Option 1: TM9 rank 8
  Option 2: TM9 rank 4
Do not define RI test for 8Rx UEs