## Slide 1: Way forward on NR UE PDSCH demodulation requirements and General aspects
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #88
Gothenburg, Sweden, 20 – 24 August 2018 Agenda Item: 7.13.1.3
R4-1811394

## Slide 2: Applicable rules for SA, NSA requirements
For single carrier SA/NSA Normal demodulation / CSI reporting performance requirements
      Reuse the test case parameters for NSA/SA requirements
      Define same minimum performance requirements for NSA/SA modes
      For NSA requirements define NR requirements only (i.e. no LTE requirements).
      Use noise-free LTE link for NSA mode
        Note: To be confirmed for FR2
Additional specific EN-DC requirements can be specified after normal requirements finalized.

## Slide 3: TDD DL/UL configuration
FR1 with SCS 30kHz
      Use configuration 7D1S2U, S = 6D:4G:4U to verify UE supporting physical features.
      Introduce additional test cases for other TDD DL-UL configurations to verify UE processing supporting different DL-UL configurations.
        Below configurations should be covered by test cases in first phase
          DDDSUDDSUU, [S1=10D:2G:2U], [S2= 10D:2G:2U]
          DDDSU, S=10D:2G:2U
        Additional test cases for other configurations will be covered once the configurations with first priority finalized
          SU, S = 12D:2G
          DDSU, S=10D:2G:2U
          DSSU, S1=10D:2G:2U, S2=12D:2G
FR2 with SCS 60 kHz: DDSU, S=11D+3G
FR2 with SCS 120 kHz: equally split test cases for below two configurations:
      DDDSU, S=10D:2G:2U
      DDSU, S=11D+3G

## Slide 4: FRCs for PDSCH test
  FR1
      64QAM Rank 2 MCS19 (64QAM table)
      256QAM Rank 1 MCS24 (256QAM table)
  FR2
      64QAM
        For rank 2, use MCS 19 or less pending on further study for PN impact
        For rank 1, use MCS 24 or less pending on further study for PN impact
      Companies are encouraged to bring more analysis for PN impact on performance requirements in FR2 covering frequency ranges from 24GHz to [52]/[40]GHz? Candidate options:
        Option 1: Define band agnostic requirements
          Assume worst case RF impairments (e.g. for 52 GHz)
          Limit the maximum tested MCS
        Option 2: Define band-specific requirements
        Other options not excluded
  TBS determination assumptions
      Noh = 0 for FR1, Noh=6 for FR2

## Slide 5: Reference Signal (DMRS, PTRS, TRS)
  DMRS
      Type 1 single symbol front loaded
      1 additional DMRS for Low (5/10Hz) and Medium (100 Hz) Speed scenarios
        i.e. for full DL slots OFDM symbols with DMRS: #2 and #9
      2 additional DMRSs for High (400 Hz) Speed scenarios
        i.e. for full DL slots OFDM symbols with DMRS: #2, #6 and #9
      FDM is applied between DMRS and data for test cases with 1 Layer and 2 Layers
  TRS
      2 slots pattern
      Periodicity 20ms
      Offset 10ms from SSB
      OFDM symbols with TRS: #4 and #8
      Bandwidth: full BWP
      0 dB boosting.
  ZP CSI-RS
      Introducing ZP CSI-RS configuration in part of test cases FFS for demod or CSI

## Slide 6: PDSCH scheduling type
  Define at least one test case for PDSCH mapping Type B. Companies are encouraged to bring proposals on the test parameters
    FR1:
      Option 1: k0 = 0, S=5, L=7 for MCS 2, DMRS type 1 single symbol with one additional DMRS (Position #5, #9)
      Other options are note precluded

## Slide 7: Normal test cases
  Performance metrics
      70% of maximum throughput
  HARQ process number and timelines
      Assume similar minimum processing time as UE side (N2) for gNB emulator to decide HARQ process number
        FDD: [4]
        TDD
          FR1, 15 kHz SCS (DDDSU): [8]
          FR1, 30kHz TDD (7D1S2U, DDDSU, DDDSUDDSUU): [8]
          FR2, 60kHz TDD (DDSU): [10]
          FR2, 120kHz TDD (DDDSU): [8]
          FR2, 120kHz TDD (DDSU): [10]
  Introduce one specific test case for LDPC graph 2:
      [6RB] allocation in the middle of CBW with MCS4
  FFS whether to define FR1 and FR2 test case for 70% test point targeting for high rank and high modulation order and 16 HARQ processes for TDD and 8 HARQ processes for FDD

## Slide 8: UE HARQ soft combing test cases
  Performance metrics
      30% of maximum throughput
  Test parameters:
      FDD and TDD
      TDD UL-DL configurations: 7D1S2U for FR1 and DDDSU/DDSU for FR2
      FRC: 16QAM Rank 1 (MCS 13)
      16 HARQ processes for TDD and 8 HARQ processes for FDD
      Channel model:
        FR1: TDL-C, 300ns and 100 Hz
        FR2: TDL-A, 30ns and [75 or 300] Hz

## Slide 9: RF impairments modeling for FR1
Use the following RF impairments models to define the minimum UE performance requirements for FR1
      TX EVM = 6% for QPSK/16QAM/64QAM
      TX EVM = 3% for 256QAM
Test equipment shall support TX EVM level not worse than the one used to define the minimum performance requirements.

## Slide 10: RF impairments modeling for FR2
Use the following RF impairments models to define the minimum UE performance requirements for FR2
  Option 1:
    Total TX EVM = [6]% for QPSK/16QAM/64QAM.
    Total TX EVM = Tx EVM due to phase noise after CPE compensation + remaining Tx EVM
    Phase noise is explicitly modelled for Tx and Rx for alignment simulations. Use phase noise model #2 as defined in TR 38.803 for FR2 demodulation performance tests.
    Remaining TX EVM in addition to Phase noise is modelled as AWGN:
      [5]% for CF 24, 29 GHz, 39 GHz, [4]% for CF 52 GHz
  Option 2:
    Total TX EVM = [6]% for QPSK/16QAM/64QAM.
    TX EVM is modelled as AWGN
    No Tx phase noise is modelled
    Phase noise is explicitly modelled for Rx. Use phase noise model #2 as defined in TR 38.803 for FR2 demodulation performance tests.
      Option 2-1: Rx Phase noise is modelled for requirements definition
      Option 2-2: Rx Phase noise is modelled only to find feasible FRC configuration (i.e. achieve maximum throughput and loss in comparison to scenarios without Rx phase noise is less then 1 dB)
  Other options are not precluded

## Slide 11: RF impairments modeling for FR2
Use option 2 from slide 10 for RAN4#88bis simulation purpose
Use the following assumptions for conformance testing for FR2
  Test equipment shall support TX EVM level not worse than the one used to define the minimum performance requirements.
  Phase noise modelling by TE
    Option 1: TX phase noise is not emulated
    Other options are not precluded

## Slide 12: SDR test
SDR test methodology
  Use the following procedure for NR SDR testing
    Calculate data rate using equation from TS 38.306 for each CA bandwidth combination from CA bandwidth combinations supported by UE, taking into account channel bandwidth size, SCS and various UE capabilities (i.e. maximum MIMO layers capability, maximum supported modulation order and scaling factor)
    Use CA bandwidth combination which allows achieving maximum data rate for SDR test
    MCS and TBS used for each CC is selected based on test parameters and on indicated UE capabilities including MIMO layers, modulation and scaling factor
      Exact MCS/TBS for SDR testing are FFS and companies encouraged to bring proposals on the MCS selection
        Option 1: Define look up table to derive MCS and TBS parameters based on UE capabilities
        Option 2: Define a procedure to derive MCS and TBS parameters based on UE capabilities
        Other options not precluded

## Slide 13: SDR test
SDR test parameters
  The channel bandwidths for SDR requirements are as follows.
    FR1, 15kHz SCS: 5, 10, 15, 20, 25, 30, 40, 50 MHz
    FR1, 30kHz SCS: 5, 10, 15, 20, 25, 30, 40, 50, 60, 80, 100 MHz
    FR2, 60kHz SCS: 50, 100, 200 MHz
    FR2, 120kHz SCS: 50, 100, 200, [400] MHz
  PDSCH Type A mapping with duration [14] OFDM symbols
  CORESET size in time domain is 1 OFDM symbol.
    FFS: CORESET size in frequency domain and FDM of CORESET and PDSCH
  List of UE MIMO layer capabilities for SDR requirements: {1, 2, 4} for FR1, and {1, 2} for FR2.
  List of supported modulation scheme for DL by the UE for SDR requirements
    FR1: up to 256QAM
    FR2: up to 64QAM
  DMRS configuration
    Option 1: No additional DMRS
    Option 2: with 1 additional DMRS
  Consider FDM of DMRS and PDSCH to increase TBS in a slot.
  PTRS will be configured for FR2,detalied for configuration FFS
  For SDR requirement, for TBS determination is set to 0 for FR1 and [6]for FR2.