## Slide 1: WF on NR PUSCH demodulation requirements
Nokia, Nokia Shanghai Bell, […]
3GPP TSG-RAN WG4 RAN#88
Gothenburg, SE, 20th – 24th Aug, 2018
Agenda: 7.13.2.2
R4-1811694
Document for: Approval

## Slide 2: Background
The following WFs were approved:
  R4-1808024, WF on NR PUSCH demodulation requirements in Rel-15 RAN4#87
  R4-1809336, WF on NR PUSCH demodulation requirements RAN#AH1807

## Slide 3: Test setup
Transmission scheme
  Define the requirements for 2 layer transmission for 2Tx
    Precoding for 2Tx 2 layer transmission
      A fixed precoder. TPMI index 0, i.e. the identity matrix, used in the test cases.
    Number of retransmission layers for 2Tx 2 layer transmission
      Fixed as 2 layers
Time domain resource
  FR1
    Slot-based transmission with resource mapping type A
    FFS:
      Slot-based transmission with resource mapping type B
      non-slot based transmission with resource mapping type B
  FR2
    Non-slot-based transmission with resource mapping type B and X UL symbols
      Number of UL symbols
        Option 1: 7
        Option 2: 4 and 2
        Option 3: 11
        Option 4: 8
        Other options not precluded
      start symbol index
        Option 1: 3
        Option 2: 2
        Option 3: 0
        Other options not precluded

## Slide 4: Test setup
DMRS configuration
  DMRS type
    Prioritize DMRS type 1 (default configuration)
    For DMRS type 2
      Define a limited number of test cases for type 2 in Rel-15 if time permits
    The test applicability for DMRS type 1 and type 2 is based on BS declaration
  EPRE ratio of PUSCH to DM-RS
    0dB
  DMRS port for 1 layer PUSCH
    port 0
  DMRS port for 2 layer PUSCH
    port 0 and 1 with frequency domain OCC
  Parameters for DMRS sequence generation
    For CP-OFDM waveform, NID =0, nSCID =0
    For DFT-s-OFDM waveform, nID =0, group hopping and sequence hopping are disabled.

## Slide 5: Test setup
PTRS are configured in FR2 test cases, the configuration is:
  Frequency density KPTRS : [2 (PTRS every 2 RBs)]
  Time density LPTRS : 1 (all symbols with PTRS)
  Default thresholds for PT-RS patterns when transform precoding is enabled
    Option1: NRB0=0, NRB1=8, NRB2=NRB3=32, and NRB4=108
    Other options not precluded.
Frequency domain resource
  DFT-S-OFDM
    Configure M contiguous PRBs in the middle of the applicable test BW, where M is the largest PRB number within the applicable test BW that satisfying M = 2α2 · 3α3 · 5α5
MCS to be used for test
  DFT-s-OFDM
    QPSK:MCS 2 (R=193/1024)

## Slide 6: Test setup
HARQ configuration
  Number of maximum HARQ transmissions
    4
  RV sequence
    {0, 2, 3, 1}
Limited buffer rate matching is disabled

## Slide 7: Simulation assumptions for simulation alignment
Parameter | value | 
 | FR1 | FR2
Transform precoding | Disabled | Disabled
Number of Tx | 1, 2 | 1
Number of Rx | 2, 4, 8 | 1, 2
Number of layers | 1, 2 | 1
Transmission scheme | Identity matrix (TPMI index 0) | -
DMRS type | type 1 | type 1
Number of DMRS symbols | 1, 1+1 | 1
symbols length | 14 | [7]
start symbol index | 0 | [0 or 2 or 3]
Time domain resource allocation type | type A | type B
Frequency domain resource | full RB allocation of the applicable BW | full RB allocation of the applicable BW
MCS index | 2, 16, 20 | 2, 16, 20
Carrier frequency (GHz) | 4 | 30
Propagation channel | TDL-A 30ns 10Hz | AWGN
SCS and BW | 15kHz: 10 30kHz: 40 | 60kHz: 100 120kHz: 100
PTRS | Not configured | Configured with KPTRS =2, LPTRS =1
Timing offset | 0 | 0
Frequency offset | 0 | 0
Code block group | Disabled | Disabled
Frequency hopping | Disabled | Disabled
Limited buffer rate matching | Disabled | Disabled
Number of HARQ transmissions | 4 | 4
Testing metric | SNR @70% of maximum throughput | SNR @70% of maximum throughput

## Slide 8: Simulation assumptions for simulation alignment
Parameter | value | 
 | FR1 | FR2
Transform precoding | enabled | enabled
Number of Tx | 1 | 1
Number of Rx | 2 | 2
Number of layers | 1 | 1
DMRS type | type 1 | Type 1
Number of DMRS symbols | [1] | [1]
symbols length | 14 | [7]
start symbol index | 0 | [0 or 2 or 3]
Time domain resource allocation type | type A | type B
Frequency domain resource | PRB Number: [50] | PRB Number: [30]
MCS index | 2 | 2
Carrier frequency (GHz) | 4 | 30
Propagation channel | TDL-A 30ns 10Hz | AWGN
SCS and BW | 30kHz: 40 | 120kHz: 100
PTRS | Not configured | [NRB0=0, NRB1=8, NRB2=NRB3=32, and NRB4=108]
Timing offset | 0 | 0
Frequency offset | 0 | 0
Code block group | Disabled | Disabled
Frequency hopping | Disabled | Disabled
Limited buffer rate matching | Disabled | Disabled
Number of HARQ transmissions | 4 | 4
Testing metric | SNR @70% of maximum throughput | SNR @70% of maximum throughput

## Slide 9: Simulation assumptions for PUSCH performance analysis with different TDD UL/DL configurations
Parameter | value
 | FR1
Transform precoding | Disabled
Number of Tx | 1
Number of Rx | 2
Number of layers | 1
TDD UL-DL configuration | 7D1S2U, S = 6D:4G:4U DDDSUDDSUU, S=10D:2G:2G DDDSU, S=10D:2G:2U
DMRS type | type 1
Number of DMRS symbols | 1+1
symbols length | 14
Time domain resource allocation type | type A
Frequency domain resource | full RB allocation of the applicable BW
MCS index | 16
Carrier frequency (GHz) | 4
Propagation channel | TDL-A 30ns 10Hz
SCS and BW | 30kHz: 40
PTRS | Not configured
Timing offset | 0
Frequency offset | 0
Code block group | Disabled
Frequency hopping | Disabled
Limited buffer rate matching | Disabled
Number of HARQ transmissions | 4
Testing metric | SNR @70% of maximum throughput