## Slide 1: 3GPP TSG-RAN WG4 Meeting #88 Gothenburg, Sweden, 20 - 24 Aug 2018
Huawei, …
Way forward on General part of NR BS demodulation performance
R4-1811726

## Slide 2: Background
The following WFs were approved:
  R4-1808022 Way forward on general part for NR BS demodulation requirements, RAN4#87
  R4-1809370 Way forward on general parameters for BS demodulatioin performance requirements, RAN4#AH1807

## Slide 3: Applicability
PRACH: Demodulation tests are defined in a channel BW agnostic way
PUSCH and PUCCH:
  For selection of the SCS and BW combination(s), the following principle will be used:
    If the SCS and BW combination(s) declared by BS are included in 38.104 with the corresponding performance requirements defined:
      If only one declared SCS and BW combination is included, then this combination is selected for test.
      If more than one declared SCS and BW combinations are included:
        For cases with smaller than [X] dB gap on simulation results for different declared SCSs, select the smallest SCS
        For cases with larger [X] dB gap on simulation results for different declared SCSs, tests all the declared SCSs
        BS is only required to pass tests for the highest channel BW declared by BS for the selected SCS(s).
    Else if the SCS and BW combination(s) declared by BS are not included in 38.104 with the corresponding performance requirements defined:
      Choose the declared SCS(s) and its nearest lower BW (i.e. reference BW) as new combination(s)
        If only one SCS and BW combination is declared, then its new combination is selected for test.
        If more than one SCS and BW combinations are declared, for those corresponding new combinations:
          For cases with smaller than [X] dB gap on simulation results for different declared SCSs, select the smallest SCS
          For cases with larger [X] dB gap on simulation results for different SCSs, tests all the declared SCSs
          BS is only required to pass tests for the selected highest nearest lower channel BW.
        the reference BW will be placed in the middle of the BW.
  Further rewording or other options not precluded.

## Slide 4: General - 1
SCS and Bandwidth
  Below bandwidth is agreed as the minimum set for BS performance requirements to be defined in Rel-15
    15kHz: 5MHz, 10MHz, 20MHz
    30kHz: 10MHz, 20MHz, 40MHz, 100MHz
    60kHz(FR2): 50MHz, 100MHz
    120kHz: 50MHz, 100MHz, 200MHz
  Additional cases requested by operators , FFS whether to define requirements
    30kHz: 50MHz, 60MHz, 80MHz
TDD UL/DL configurations
  Just consider those TDD UL DL configurations from the operators’ input as listed in Annex.
  Companies are encouraged to analyze the PUSCH performance requirements for different TDD UL/DL configurations
    Compare the simulation results for the following TDD UL/DL configurations for one PUSCH case with 30kHz SCS for investigation:
      7D1S2U, S = 6D:4G:4U
      DDDSUDDSUU, S=10D:2G:2U
      DDDSU, S=10D:2G:2U
      Note: No PUSCH transmission on special slot in the simulations.
    If the results are similar for those three UL DL configurations, one UL/DL configuration will be used for each SCS, and the UL/DL configurations used in BS RF will be considered as baseline.

## Slide 5: General - 2
Phase Noise
  FFS whether PN is modelled in FR2 simulation
    Companies are encouraged to provide simulation results both with and without phase noise modelling in different high frequency ranges (such as 30GHz) and specific phase noise model defined in TR38.803.
Antenna configuration for FR1
  Not to include requirements for BS with >8 antenna connectors
  FFS how to conduct test for BS with > 8 antenna connectors, companies are encouraged to bring inputs for the next RAN4#88bis meeting.
EN-DC:
  Further discuss whether to have specific tests for EN-DC in BS demodulation part in the next meeting.

## Slide 6: Channel Model
FR1
  Reuse the conclusions from UE demodulation discussions
FR2
  Option 1: Reuse the conclusions from UE demodulation performance discussion
    TE vendors and interested companies are invited to check if the channel model used by UE demodulation performance is applicable for BS demodualtion performance test.
  Other options not precluded

## Slide 7: Annex