## Slide 1: 3GPP TSG-RAN WG4 Meeting #88 Gothenburg, Sweden, August 20~August 24, 2018
Ericsson
Way forward on NR PRACH demodulation requirements
R4-1811728

## Slide 2: PRACH requirements
There are no test cases for Restricted sets in Rel-15
Preamble Format (For Rel-15)
  For long sequence, requirements are defined for:
    [Format 0]
  For short sequence, requirements are:
    [A1, A2, A3, B4, C0 and C2]
SCS:
  Keep the previous agreement and cover 15kHz, 30kHz, 60KHz (FR2) and 120KHz for short sequence
  Apply the performance requirements for short sequence based on BS declaration

## Slide 3: PRACH requirements
Timing offset
  For conformance test, we reuse the LTE timing offset scheme for preamble transmission, i.e.,
    The timing offset base value is set to 50% of Ncs. This offset is increased within the loop, by adding in each step a value of [0.1us], until the end of the tested range, which is [0.9us]. Then the loop is being reset and the timing offset is set again to 50% of Ncs.
  Frequency offset
    Frequency offset for FR1
      Option 1: 500 Hz
      Other options are not precluded

## Slide 4: PRACH requirements
Logical sequence index
  Option 1: 22 for long sequence, 0 for short sequence
    Note that this resulting in root sequence = 1 for both long and short sequences.
  Other options not precluded
Ncs
  Long sequence: 13
  Short sequence:
    Option 1: 46 for FR1, 0 for FR2
    Option 2: 23 for FR1, 69 for FR2
    Option 3: 0 for FR1, 0 for FR2
    Other options are not precluded
    Intension next meeting to narrow to one option for requirement

## Slide 5: PRACH requirements
  Test metrics
    False alarm probability and detection probability
      Reuse the LTE metric of 0.1% false alarm probability and 99% detection probability.
    Time estimation error
      For AWGN channel
        reuse the LTE metric of 1.04us
      For fading channel
        Need further study

## Slide 6: Simulation Assumption for simulation alignment
SCS
  15kHz
  30kHz
  60KHz (FR2)
  120KHz
Channel:
  AWGN
Antenna configuration
  1 Tx, 2 Rx
Ncs (Intension next meeting to narrow to one option for requirement)
  Option 1:
    Format 0: Ncs=13 and v=32
    Short sequences
      Ncs=23 for FR1
      Ncs=69 for FR2
      v = [0]
  Option 2:
    Format 0: Ncs=13 and v=22
    Short sequences
      Ncs=46 for FR1
      Ncs=0 for FR2
      v = [0]
  Option 3:
    Format 0: Ncs=13 and v=32
    Short sequences
      Ncs=0 for FR1 and FR2
      v = [0]

## Slide 7: Appendix
Ncs
 | Burst format | China Telecom | Samsung | Nokia | Huawei | Ericsson
FR1 | 0 | 13 |  | 13 | 23 for FR1 | 13
 | 2 | 167 |  |  |  | 
 | 3 | 0 |  |  |  | 
 | A1 | 10 | 0 for short sequence |  |  | Ncs=46 for 30KHz SCS
 | A2 |  |  | 46 |  | 
 | A3 |  |  |  |  | 
 | B4 | 46 |  | 46 |  | 
 | C0 |  |  |  |  | 
 | C2 | 0 |  | 46 |  | 
FR2 | A1 | 10 | 0 for short sequence |  | 69 for FR2 | 0 for FR2
 | A2 |  |  | 69 |  | 
 | A3 |  |  |  |  | 
 | B4 | 46 |  | 69 |  | 
 | C0 |  |  |  |  | 
 | C2 | 0 |  | 69 |  | 

## Slide 8: Appendix
V
 | Burst format | China Telecom | Nokia
FR1 | 0 | 32 | 32
 | 2 | 2 | 
 | 3 | 0 | 
 | A1 | 6 | 
 | A2 |  | 0
 | B4 | 1 | 0
 | C2 | 0 | 0
FR2 | A1 | 6 | 
 | A2 |  | 0
 | B4 | 1 | 0
 | C2 | 0 | 0