## Slide 1: Way forward on NR PBCH demodulation requirements
Huawei, HiSilicon, China Telecom, CMCC, NTT DOCOMO, Vodafone, Orange, Sprint, AT&T, KDDI, SoftBank, Deutsche Telekom, Nokia, Nokia Shanghai Bell, SK telecom
3GPP TSG-RAN WG4 Meeting #88 R4-1811730
Gothenburg, Sweden, Aug 20 – 24th, 2018
Agenda Item: 7.13.1.4

## Slide 2: Agreements
RAN4 introduces the PBCH demodulation requirements in Rel-15.
  Note the PBCH demodulation requirements do not need to be tested in RAN5 as same as LTE PBCH demodulation requirements.
Test metric:
  SNR_PBCH@1% Pm-bch. Pm-bch is defined as 1-A/B, where A is the number of correctly decoded MIB PDUs and B is the number of transmitted MIB PDUs.
  UE combines the PBCH symbols of the same SSB index within the MIB TTI (80ms).
Interested companies are encouraged to provide the simulation results in RAN4#88bis.
  Companies may prioritize other physical channel (PDSCH and PDCCH), and CSI reporting.

## Slide 3: Simulation assumptions
Parameters | Unit | Value
Cell ID |  | 0
CP length |  | Normal
Number of SS/PBCH blocks within an SS burst set periodicity |  | 1
SS/PBCH block index |  | 0
SS burst periodicity | ms | 20
MIB size | bits | 24
PBCH payload size (including 24 bits CRC and 8 bits of SS/PBCH location information) | bits | 56
Receiver assumption |  | LMMSE
Table 1: common parameters
For PBCH demodulation requirements
  The simulation assumptions in Table 1 are subject to common setup
  The simulation assumptions in Table 2 are subject to alignment purpose

## Slide 4: Simulation assumptions
Parameters | Test 1 | Test 2 | Test 3 | Test 4
Frequency Range | FR1 | FR1 | FR2 | FR2
Channel Bandwidth | 10MHz | 40MHz | 100MHz | 100MHz
SS/PBCH SCS | 15kHz | 30kHz | 120kHz | 240kHz
SS Block pattern (Note 1) | Case A | Case B Case C | Case D | Case E
Antenna Configuration (Note 2) | 1x2 1x4 | 1x2 1x4 | 1x2 | 1x2
Propagation channel (Note 3) | TDL-C RMS DS=300ns Doppler=100Hz | TDL-A RMS DS=30ns, Doppler=10Hz | FFS | FFS
Table 2: Test cases for PBCH demodulation
Note 1: Depending on the operating band. Refers to TS38.101-1 Table 5.4.3.3-1 for which band uses which pattern
Note 2: Define two sets of demodulation performance requirements separately for 2Rx and 4Rx
Note 3: Use PDP specified in TS38.901