## Slide 1: Way forward on specifying NR demodulation
Anritsu, Rohde & Schwarz, Keysight, Spirent,
Qualcomm
3GPP TSG-RAN WG4 Meeting#88
Gothenburg, Sweden, 20–24 August, 2018
R4-1811776

## Slide 2: Requirements to be specified in TS 38.101-4
Absolute Noc level at -153dBm/Hz at Reference point, for bands up to 40GHz
SNR at Reference point, test-specific value
Downlink signal and noise aligned to the Rx beam peak

## Slide 3: Reference point SNR and Baseband SNR
Principle of calculation:
  Set wanted noise to give 1dB difference between Reference point SNR and Baseband SNR, using agreed UE parameters
  1dB difference is a fixed value, and applies across range of +ve and –ve SNR values

## Slide 4: Assumptions on UE parameters
Values derived from UE assumptions for EIS defined in R4-1804589, 39GHz
  Used together with 1dB difference between Reference point SNR and Baseband SNR, to derive Noc level of -153dBm/Hz at Reference point
  Tradeoff between parameters is UE implementation choice
  A UE type with significantly different parameters would result in a different Noc level, but maintain 1dB difference between Reference point SNR and Baseband SNR

## Slide 5: Maximum feasible SNR level
Values derived from Test system assumptions agreed by TE vendors
  These are UE baseband SNR values. Figures used in TS 38.101-4 will be 1dB higher
  Values based on currently foreseen test equipment limitations