## Slide 1: WF on beam correspondence
Qualcomm, Sony
3GPP TSG-RAN WG4 Meeting #88 R4-1811805
Gothenburg, Sweden, 20th – 24th Aug, 2018
Agenda item: 7.6.16.3

## Slide 2: Background (from RAN4 #86bis)
The following Way Forward was approved in RAN4 #86bis:
Agreement:
Beam correspondence requirement should be only based on UE Tx EIRP measurements performed by the TE.
Beam correspondence requirements definition will be further discussed based on the following two approaches, [other approaches not precluded]:
  1st approach: define the beam correspondence requirement based on an EIRP tolerance between the best Tx beam and the Tx beam selected based on DL measurements.
  2nd approach : define the beam correspondence requirement based on EIRP CDF requirements. In this case, the correspondence is defined based on passing the EIRP CDF requirements without UL Tx beam sweeping.
  Companies provide their preferred approach at next RAN4 meeting
RAN4 will define a beam correspondence requirement based on bullets 1, 2
RAN4 will decide if beam correspondence RF requirement can be tested simultaneously with other Tx requirements.
* Whether it is mandatory or not for beam correspondence is up to decision of RAN1 and RAN

## Slide 3: Discussion and agreements in RAN4 #88
Two ad hoc minutes were held (R4-1811523 and R4-1811803)
  Several issues were discussed in RAN4 #88 with the following agreements:
  The agreement for PC3:
    1st approach: Study this and solve identified possible issues in Rel16. How to address this is further discuss in this meeting. Also other approaches should not be precluded.
    2nd approach: Specify this in Rel15
      For PC3, beam correspondence implies that both spherical coverage and minimum peak EIRP are met

## Slide 4: Open issues
The following list of open issues were identified:
  Requirement for power classes different from PC3:
    How to handle the requirement for these power classes
  Assumption on DL signal:
    Option 1 (only SSB) vs. Option 2 (both SSB and CSI-RS)
    Polarization of DL signals
  SRS configuration:
    The link does not use any SRS configuration
  Testability:
    Implications of including beam peak in BC requirement and potential EIRP CDF measurement grid optimization
  UL polarizations:
    Whether the requirements shall be met with both UL polarizations active

## Slide 5: Way forward
In RAN4 #88bis
  The open issues listed in slide 5 should be addressed
  A draft CR introducing the beam correspondence requirement in TS 38.101-2 should be approved

## Slide 6: References (from RAN4 #88)
R4-1805703, “WF on beam correspondence test methodology at FR2”, LGE, Qualcomm, and MediaTek, 3GPP RAN4 #86bis, April, 2018.
R4-1809789, “Views on Beam Correspondence”, Apple Inc.
R4-1809790, “Draft CR to TS 38.101-2: Introduction of the requirement on beam correspondence”, Apple Inc.
R4-1809839, “Beam Correspondence in FR2”, Intel Corporation.
R4-1810237, “FR2 UE beam correspondence requirement”, MediaTek Inc.
R4-1810427, “Relationship for the beam correspondence and spherical EIS requirements at FR2”, LG Electronics France
R4-1810429, “CR for introducing of beam correspondence and spherical EIS RF requirements in TS38.101-2”, LG Electronics France
R4-1811020, “Draft CR to 38.101-2: FR2 EIRP and Beam Correspondence Requirement”, Qualcomm. Incorporated.
R4-1811206, “On beam correspondence”, Huawei, HiSilicon.
R4-180xxxx, “RAN4#87 Meeting report,” ETSI MCC.
R4-1811023, “On FR2 Spherical Coverage EIS Requirement”, Qualcomm Incorporated.
R4-1810065, “On EIS Spherical Coverage for FR2 UEs”, Apple.
R4-1811523, “Beam Correspondence Ad Hoc minutes”, Qualcomm Incorporated.
R4-1811803, “FR2 beam correspondence second adhoc minutes”, Apple.