## Slide 1: WF on ACS, IBB and OBB for intra-band contiguous CA for FR1
Intel, …
3GPP TSG-RAN WG4#88 Meeting R4-1811806
Gothenburg, SE, 20th – 24th August 2018

## Slide 2: Background
The definition of ACS, IBB and OBB for intra-band contiguous CA with two component carriers has been introduced in TS 38.101-1.
However, the definition for intra-band contiguous CA for these requirements consider only the BW Class C.
ACS, IBB and OBB requirements for intra-band contiguous CA for two components carriers for the BW B and BW F are missing

## Slide 3: CA BW Class definition for FR1
NR CA bandwidth class | Aggregated channel bandwidth | Number of contiguous CC | Fallback group
A | BWChannel_CA ≤ BWChannel,max | 1 | 
B | 20 MHz ≤ CBW ≤ 50 MHz | 2 | 
C | 100 MHz < BWChannel_CA ≤ 2 x BWChannel,max | 2 | 1
D | 200 MHz < BWChannel_CA ≤ 3 x BWChannel,max | 3 | 
E | 300 MHz < BWChannel_CA ≤ 4 x BWChannel,max | 4 | 
F | 50 MHz < BWChannel_CA ≤ 100 MHz | 2 | 2
G | 100 MHz < BWChannel_CA ≤ 150 MHz | 3 | 
H | 150 MHz < BWChannel_CA ≤ 200 MHz | 4 | 
I | 200 MHz < BWChannel_CA ≤ 250 MHz | 5 | 
J | 250 MHz < BWChannel_CA ≤ 300 MHz | 6 | 
K | 300 MHz < BWChannel_CA ≤ 350 MHz | 7 | 
L | 350 MHz < BWChannel_CA ≤ 400 MHz | 8 | 
NOTE: BWChannel, max is maximum channel bandwidth supported among all bands in a release |  |  | 

## Slide 4: NR CA configuration combinations set for BW B and BW F
In TS 38.101-1 has been defined the NR CA configuration combinations set for BW Class F for n77, n78, n79 as follows:
The latest TS 38.101-1 does not yet consider the NR CA configuration combination set for BW Class B
NR CA configuration | Uplink CA configurations | Component carriers in order of increasing carrier frequency |  |  | aggregated bandwidth [MHz]
 |  | Channel bandwidths for carrier (MHz) | Channel bandwidths for carrier (MHz) | Channel bandwidths for the other carrier (MHz) | 
CA_n77F, CA_n78F, CA_n79F |  | 40 | 20 |  | 60
 |  | 50 | 20 |  | 70
 |  | 40 | 40 |  | 80
 |  | 40 | 50 |  | 90
 |  | 50 | 50 |  | 100

## Slide 5: WF for definition of ACS, IBB and OBB requirements for intra-band contiguous CA
In order to keep consistency in the TS 38.101-1 for intra-band contiguous for two components, the following options should be considered:
  Option 1:
    Remove intra-band contiguous CA configuration combinations set for BW Class B and BW F in Rel-15 and define in Rel-16
    Remove ACS, IBB and OBB requirements for intra-band contiguous CA for BW Class B and F in Rel-15 and define in Rel-16
  Option 2:
    Mantain intra-band contiguous CA configuration combinations set for BW Class B and BW F in Rel-15
    Define ACS, IBB and OBB requirements for intra-band contiguous CA for BW Class B and F in Rel-15
    Unless agreement is not reached on ACS, IBB and OBB requirements remove BW Class B and F at the end of RAN4#89
Companies are encouraged to clarify the feasibility of both options