## Slide 1: Handling of receiver requirements in EN-DC
Qualcomm
3GPP TSG-RAN WG4 Meeting #88 R4-1811814 Gothenburg, Sweden, 20th – 24th Aug, 2018

## Slide 2: Background
Receiver requirements as discussed in R4-1811027 are unclearly or not specified in TS 38.101-3
Agreements:
  Proposal 1: RAN4 will discuss and agree receiver requirement handling for EN-DC mode in following meeting and dedicated agenda item will be opened.
  Proposal 2: RAN4 will inform RAN5 that RAN4 will conclude the receiver requirements in the RAN4#88Bis and #89
RAN5 needs clarifications on what and how to test these missing requirements
Discussion indicated that treatment of inter-band and intra-band could be different

## Slide 3: WF for general requirement handling in 38.101-3
Stand alone transmitter and receiver requirement in TS 38.101-1 and TS 38.101-2 are applied unless exceptions are specified in TS 38.101-3 except for REFSENS and OOB. OOB will be specified for EN-DC in upcoming meetings
Situation will be clarified in TS 38.101-3 with following statements:
Section 4.1:
  Terminal that supports EN-DC configuration shall meet E-UTRA requirements as specified in TS 36.101 [4] and NR requirements as in TS 38.101-1 [2] and TS 38.101-3 [3] unless otherwise specified in this specification
Section 7.1:
  Unless otherwise stated, requirements for NR receiver written in TS 38.101-1 and TS 38.101-2 apply and are assumed anchor agnostic. Requirements are verified under conditions where anchor resources do not interfere NR operation
Section 6.1:
  Unless otherwise stated, requirements for NR transmitter written in TS 38.101-1 and TS 38.101-2 apply and are assumed anchor agnostic. Requirements are verified under conditions where anchor resources do not interfere NR operation

## Slide 4: Way Forward for EN-DC inter-band
For UE’s that do support SA, requirements are verified in SA mode for NR and performance is assumed to be EN-DC combination agnostic except for REFSENS and OOB. OOB will be specified for EN-DC in upcoming meetings
For UE’s that do not support SA i.e. they can only establish connection with the help from LTE anchor, requirements can be verified by either of two methods:
  1) choosing an anchor band and channel that does not interfere with NR performance or
  2) by first establishing connection and then disabling all resources from anchor RAT, meaning DL/UL scheduling and SRS/CQI disabled and this way ensuring presence of anchor does not interfere NR performance

## Slide 5: Way Forward for EN-DC intra-band
SA mode requirements may not be applicable if UE is configured for EN-DC
Intra-band receiver requirements will be defined for EN-DC mode