## Slide 1: WF on NR PUSCH demodulation requirements
Nokia, Nokia Shanghai Bell, […]
3GPP TSG-RAN WG4 RAN#88
Gothenburg, SE, 20th – 24th Aug, 2018
Agenda: 7.13.2.2
R4-1810884
Document for: Approval

## Slide 2: Test setup
Transmission scheme
  The precoding matrix of TPMI index [0] can be used in the demodulation test
DMRS configuration
  The performance requirement for DMRS type 2 can be considered in future release if needed
PTRS configuration
  KPTRS : [4]
  LPTRS : [1]
Time domain resource
  FR1 and FR2:
    Slot based transmission with resource mapping A
    Non-slot based transmission with resource mapping B and UL symbols is [11]
MCS
  The requirements for pi/2-BPSK can be considered with DFT-s-ODFM together only after the tests for CP-OFDM is finished.
Limited buffer rate matching is disabled

## Slide 3: Test case definition
Parameter | value | 
 | FR1 | FR2
Transform precoding | Disabled | Disabled
Number of Tx | 1, 2 | 1
Number of Rx | 2, 4, 8 | 1, 2
Number of layers | 1, 2 | 1
Transmission scheme | Corresponding precoding matrix of TPMI index [0] | -
DMRS type | type 1 | type 1
Number of DMRS symbols | 1, 1+1 | 1
symbols length | 11, 14 | 11, 14
Time domain resource allocation type | type A , type B | type A , type B
Frequency domain resource | full RB allocation of the applicable BW | full RB allocation of the applicable BW
MCS index | 2, 16, 20 | 2, 16, 20
Carrier frequency (GHz) | 4 | 30
Propagation channel | TBD | TBD
SCS and BW | 15kHz: 10 30kHz: 20/40/100 | 60kHz: 100 120kHz: 100
PTRS | Not configured | Configured with KPTRS =4, LPTRS =1
Timing offset | 0 | 0
Frequency offset | 0 | 0
Code block group | Disabled | Disabled
Frequency hopping | Disabled | Disabled
Limited buffer rate matching | Disabled | Disabled
Number of HARQ transmissions | 4 | 4
Testing metric | SNR @70% of maximum throughput | SNR @70% of maximum throughput

## Slide 4: Test case definition
Parameter | value | 
 | FR1 | FR2
Transform precoding | enabled | TBD
Number of Tx | TBD | TBD
Number of Rx | TBD | TBD
Number of layers | 1 | TBD
DMRS type | type 1 | TBD
Number of DMRS symbols | 1, 1+1 | TBD
symbols length | 11, 14 | TBD
Time domain resource allocation type | type A , type B | TBD
Frequency domain resource | full RB allocation of the applicable BW | full RB allocation of the applicable BW
MCS index | TBD | TBD
Carrier frequency (GHz) | 4 | 30
Propagation channel | TBD | TBD
SCS and BW | 15kHz: 10 30kHz: 20/40/100 | TBD
PTRS | Not configured | TBD
Timing offset | 0 | 0
Frequency offset | 0 | 0
Code block group | Disabled | Disabled
Frequency hopping | Disabled | Disabled
Limited buffer rate matching | Disabled | Disabled
Number of HARQ transmissions | 4 | 4
Testing metric | SNR @70% of maximum throughput | SNR @70% of maximum throughput