## Slide 1: Transient timing clarifications for EN-DC mode
Qualcomm, Huawei
3GPP TSG-RAN WG4 Meeting #88 R4-1811464
Gothenburg, Sweden, 20th – 24th Aug, 2018

## Slide 2: Background
Agreement in chairman notes:
  ftp://10.10.10.10/RAN/RAN4/Inbox/Chairman_Notes/RAN4%2388-UE%20RF_Chairman_report%20_1-0.zip
  Proposal 3: Intra-band contiguous transient periods are applied similarly as 0 usec case for ULSUP-TDM.
  Proposal 4: For inter-band EN-DC in SUO or dynamic TDM mode, transient periods follow each other and are inclusive in the corresponding slots.
Open items remains for this WF:
  1) Transient period locations and switching time details for switching between NR UL and SUL
  2) Transient period locations and switching time details for EN-DC for non-contiguous channel allocations (DC_3_n3 case)
  3) Switching time location for ULSUP

## Slide 3: Background---Switching time cases in EN-DC
LTE/NR switching time
  Inter-band EN-DC with ULSUP TDM mode: specified in TS38.101-3 but need to align with other switching time related requirement
  Intra-band case:
    Contiguous: addressed and agreed in proposal 3 in R4-1810981
    Non-contiguous: addressed in proposal 2 in R4-1810981 but still open (DC_3_n3)
  Inter-band case: addressed and agreed in proposal 4 in R4-1810981
NR UL/SUL switching time
  Inter-band EN-DC with SUL
    NR SUL and LTE operating in ULSUP TDM mode: switching time 0us
    NR SUL and LTE operating in different bands: switching time 140us
NR D/U pattern | D | D | D | S | U | D | D | S | U | U
NR UL |  |  |  |  | NR UL |  |  |  | NR UL | NR UL
NR SUL |  |  |  | NR SUL |  | NR SUL |  |  |  | 
LTE UL |  |  | LTE UL |  |  |  |  | LTE UL |  | 
LTE TDM pattern | D | S | U | D | D | D | S | U | D | D
NR UL/SUL switching
LTE/NR switching
LTE/NR switching

## Slide 4: Way Forward for LTE/NR switching for inter-band EN-DC with SUL
When SUL is configured for same band with LTE in EN-DC for same UE, Rel-15 only defines case when SUL channel configuration is same as LTE channel configuration
  Clarification: This is ULSUP and ULSUP requirements apply
  Time mask for LTE and NR switching for ULSUP TDM should be changed for type 2 UE to separate the transient period and switching time and move the switching time of 20us always in NR slot to ensure LTE system performance as follows:

## Slide 5: Way Forward for NR UL/SUL switching
When SUL is configured for same band with LTE and there is one LTE band in EN-DC for same UE, 0 usec switching time applies between NR UL and NR SUL
When SUL is not the same band as LTE or there is more than one LTE band, 140 usec switching time applies between NR UL and NR SUL
Transients and switching times are applied as follows:
NR SUL
NR UL
Slot boundary
0 or 140 usec OFF power
10 usec
10 usec
NR UL
NR SUL
Slot boundary
0 or 140 usec OFF power
10 usec
10 usec

## Slide 6: WF for Intra-band non-contiguous EN-DC in SUO mode Case 1 for DC_3_n3
120 usec is allowed for switching and transients are additive to the switching time
  Some improvements on the switching time can be further discussed based on different architectures in Rel.16
EUTRA
NR
Slot boundary
120 usec OFF power
20 usec
10 usec
NR
EUTRA
120 usec OFF power
10 usec
20 usec
Slot boundary