## Slide 1: WF on Remaining issues on NR ON/OFF time masks
vivo, …
3GPP TSG-RAN WG4#88 Meeting R4-1811471
Gothenburg, SE, 20th – 24th August 2018

## Slide 2: Background
A number of issues still remains for ON/OFF mask.

## Slide 3: Q1: Whether a capability should be introduced or not.
Option 1: Keep current scheme (no capability) and conditions for blanking.
Option 2: Introduce a UE capability for transient time parameter.
  BS can use this parameter to judge whether blanking is needed or not.
Option 3:Allow opportunistic recovery of the gap symbols without signaling.
  Remove blanking scheme and revise the transient period location to be equally split between the symbol boundaries

## Slide 4: Q2: Power Change limitation
The number of transient period inside a slot (or a subslot)
  Option 1: Not be limited;
  Option 2: Limit to a certain number (e.g. [X] times for a specific SCS);

## Slide 5: Q3: RB hopping / frequency hopping
Currently it is not clarified whether a transient period is needed for RB hopping / Frequency hopping and the corresponding definition.
Clearly defined the condition which the transient period applies.
  Both power change and RB hopping will need a transient period.

## Slide 6: Q4: Consecutive short subslot and DMRS
Remove the current requirement condition in Figure 6.3.3.9-2 “Consecutive short subslot transmissions time mask where DMRS is not the first symbol in the adjacent short subslot transmission”.
  Revise the “Consecutive short subslot transmissions time mask” and transient period equal split between short subslot boundaries

## Slide 7: Q5: Consecutive Long Subslot transmission requirements
For the case of two long consecutive subslots, equally split the transient period, do not differentiate DMRS with data symbols.

## Slide 8: Q6: CA requirements
FFS: [In intra-band CA, the rules for the carrier with short length channel previal over those of the other CCs.]
Will be developed in Rel-15.