## Slide 1: WF on UE feature list
NTT DOCOMO
GPP TSG RAN WG4 Meeting #8 R4-1811530
Gothenburg, Sweden, 20th – 24th August, 2018

## Slide 2: Background
The followings are discussed during RAN4 #88
  RAN4 related UE features for SA:
    Multiple frequency band indication
    Modified MPR behavior
    Multiple NS/P-Max
    Maximum uplink duty cycle
    Short Measurement Gap
  RAN4 responsible features in RAN1 feature list [RP-181483]
  DL/UL MIMO layer proposed in [R4-1810875]

## Slide 3: Multiple frequency band indication
Offline agreement on Wed
Proposal
  Option 1: Mandatory with capability similar to LTE
  Option 2: Mandatory without capability
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know whether the feature is supported by the UE (what happens if gNB does not know?) | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN
2-11 | Multiple frequency band indication | 1) Multiple frequency band indication |  | Yes | UE does not support multiple frequency band indication | Type 4 | No Need | No Need |  | Per UE capability | RAN4 | TBD

## Slide 4: Modified MPR behavior
RAN2 already introduced UE capability but there are two remaining parts
Proposal
  No FDD/TDD and FR1/FR2 differentiation
  Optional feature
Definitions for parameters | Per | M | FDD TDD DIFF
modifiedMPR-Behaviour Indicates whether the UE supports modified A-MPR due to some reasons e.g. regulatory requirements change, RB restriction is replaced to A-MPR for better frequency usage efficiency. | Band | Tbd | Tbd
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know whether the feature is supported by the UE (what happens if gNB does not know?) | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN
2-12 | Modified MPR behaviour | 1) Modified MPR behaviour |  | Yes | UE does not support modified MPR behaviour | Type 1 | No Need | No need |  | Per band capability | RAN4 | Optional

## Slide 5: Multiple NS/P-Max
Offline agreement on Wed
Proposal
  Confirm offline agreement
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know whether the feature is supported by the UE (what happens if gNB does not know?) | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN
2-13 | Multiple NS/P-Max | 1) Multiple NS/P-Max |  | Yes | UE does not support multiple NS/P-Max | Type 4 | No Need | No need |  | Per UE capability | RAN4 | Mandatory without capability

## Slide 6: Maximum uplink duty cycle
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know whether the feature is supported by the UE (what happens if gNB does not know?) | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN
2-134 | Maximum uplink duty cycle for FR1 power class 2 UE | 1) Maximum percentage of uplink symbols can be scheduled within 10msa certain evaluation period. The value range is {50%, 60%, 70%, 80%, 90%, 100%}. If the field is absent, 50% shall be applied. |  | Yes | The network cannot know maximum percentage of uplink symbols can be scheduled for high power UE (e.g. i.e. power class 2 UE) | Type 1 | No Need | Applicable only to FR1 power class 2 UE |  | Per band capability. If this capability is absent and the percentage of uplink symbols transmitted in 10ms a certain evaluation period is larger than 50%, or this capability is not absent and the percentage of uplink symbols transmitted in 10ms a certain evaluation period is larger than this capability, apply all requirements for the default power class. The evaluation period is up to UE implementation, no less than one radio frame. UE do not need to do UL duty cycle calculation when it’s transmit power is below 23dBm and all the UL/DL configurations can be scheduled. | RAN4 | Optional
Proposal: Agree the following description

## Slide 7: Maximum uplink duty cycle
Proposal:
  Option 1: Introduce 40%
  Option 2: No need to introduce 40%

## Slide 8: Short Measurement Gap
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know whether the feature is supported by the UE (what happens if gNB does not know?) | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN
3-3 | Short Measurement Gap | 1) Short measurement gaps (pattern#2 and #3) are supported in NR standalone operation for LTE measurement |  | Yes | UE does not support short measurement gap pattern#2 and #3 in NR standalone operation for LTE measurement | Type 4 | No need | No need |  | Per UE capability | RAN4 | optional
Proposal: Agree the following description
Notes: R4-1807971

## Slide 9: General
Offline agreements
  The following features will be removed from RAN1 feature list since those are already covered by RAN4 feature list
    0-3 DL modulation scheme (only note column)
    0-5 pi/2-BPSK for PUSCH
    0-6 64QAM for PUSCH
    0-7 256QAM for PDSCH
    0-8 256QAM for PUSCH
    0-9 Subcarrier spacings and FFT size in conjunction with supportable BW with normal CP
    0-11 pi/2-BPSK for PUCCH format 3/4
    0-14 [1-symbol GP for 120KHz SCS in unpaired spectrum]
    6-15 7.5kHz UL raster shift
    6-20 Simultaneous reception and transmission on different carriers for each band combination
  FFS for other features
    0-12 Non-contiguous UL PRB CP-OFDM per CC
    1-11 Support of CSI-RS RRM measurement for SCell without SS/PBCH block
    2-55 SRS Tx switch
    2-56 SRS carrier switch
    4-1 Basic UL control channel
Proposal
  Send LS to RAN1 to remove above features (0-3, 0-5, 0-6, 0-7, 0-8, 0-9, 0-11, 0-14, 6-15, 6-20) from RAN1 feature list

## Slide 10: Non-contiguous UL PRB CP-OFDM per CC
Offline outcome on Wed
Progress in UE RF session
  CR for almost contiguous UL CP-OFDM was approved (R4-1811474)
Proposal
  Remove this feature from RAN1 feature list. Inform RAN1 that Non-contiguous UL PRB CP-OFDM per CC is not supported in Rel-15
  Approve almost contiguous as optional feature in RAN4 feature list as follows
Features | # | Feature group | Components | Type (see R2-1712078) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | Note | Responsible WG | RAN WG recommendation | Proposal
 | 0-12 | Non-contiguous UL PRB CP-OFDM per CC | When VRB-to-PRB mapping is used, PRB is after interleaving | RAN4 to decide | RAN4 to decide | RAN4 to decide | It is up to RAN4 to decide | RAN4 |  | Proposal: Remove this feature from RAN1 feature list and discuss “almost contiguous UL CP OFDM” => Wait decision for almost contiguous UL CP-OFDM
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know whether the feature is supported by the UE (what happens if gNB does not know?) | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN
2-7 | Almost contiguous UL CP-OFDM | 1) Support of almost contiguous UL CP-OFDM transmissions |  |  | UE does not support almost contiguous UL CP-OFDM | Type 4 | No need | Yes |  | RAN4 had does not defined the requirements for “Almost contiguous UL CP-OFDM” in Rel-15. RAN4 will continue to discuss the definition of “Almost contiguous UL CP-OFDM”. | RAN4 | TBD Optional

## Slide 11: Support of CSI-RS RRM measurement for SCell without SS/PBCH block
Offline outcome on Wed
Proposal
  Define this feature as optional
Features | # | Feature group | Components | Type (see R2-1712078) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | Note | Responsible WG | RAN WG recommendation | Proposal
 | 1-11 | Support of CSI-RS RRM measurement for SCell without SS/PBCH block |  | Type 3 | N. A. | N.A. | RAN4 to check |  |  | Proposal: Define feature as optional. =>FFS

## Slide 12: SRS Tx switch
Offline outcome on Wed
Proposal
  No further action in terms of UE feature list
Features | # | Feature group | Components | Type (see R2-1712078) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | Note | Responsible WG | RAN WG recommendation | Proposal
 | 2-55 | SRS Tx switch | 1. Support SRS Tx port switch, 2. Report whether the uplink TX switching impact to downlink receiving in a band, | Type 3 | N.A. | N.A. | Component-2 is agreed with conditioned to RAN4’s decision.— | RAN1/4 | Component-1 is a list of TRx pairs, candidates are {1T2R, 1T4R, 2T4R, 1T4R/2T4R} Component-2: Candidate value set:, {yes, no}, | Proposal: Define feature as optional for UE to support FFS

## Slide 13: SRS carrier switch
Offline outcome on Wed
Progress until RAN4 #88
  Candidate value sets: RAN4 sent LS to RAN1 (R1-1805817/R4-1805660)
  Signaling granularity: RAN4 sent LS to RAN1 to change granularity (R4-1811534, Type1->Type3, and separate DL/UL signaling)
Proposal
  No need further action in terms of UE feature list
Features | # | Feature group | Components | Type (see R2-1712078) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | Note | Responsible WG | RAN WG recommendation | Proposal
 | 2-56 | SRS carrier switch | 1. Report inter-cell switching time capability | Type 1 | No need | N.A. |  | RAN1/4 | candidate values set is up to RAN4 RAN4 reply LS, R1-1805817, includes candidate value sets | Proposal: Further discuss the SRS carrier switch UE capability signalling granularity. Define feature as optional for UE to support. FFS

## Slide 14: Basic UL control channel
Offline outcome on Wed
Features | # | Feature group | Components | Type (see R2-1712078) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | Note | Responsible WG | RAN WG recommendation | Proposal
 | 4-1 | Basic UL control channel | 1) PUCCH format 0 over [1]-2 OFDM symbols once per slot with FH 3) PUCCH format 1 over [4] – 14 OFDM symbols once per slot with frequency-hopping 5) One SR configuration per PUCCH group 6) HARQ-ACK transmission once per slot with its resource/timing determined by using the DCI 7) Multiplexing of SR and HARQ-ACK on a PUCCH 8) HARQ-ACK piggyback on PUSCH 9) Semi-static beta-offset configuration for HARQ-ACK | N.A. | N.A. | N.A. | RAN4 to check feasibility of frequency hopping for PUCCH formats for FR2 |  | Mandatory without capability signaling | Proposal: RAN4 to further discuss whether to introduce transition time requirements for PUCCH frequency hopping in FR2 or whether to introduce a new UE capability.  FFS

## Slide 15: Basic UL control channel
Proposal
  FFS: feasibility of frequency hopping for PUCCH formats for FR2

## Slide 16: MIMO layer related
Proposals in [R4-1810875]
  Proposal 1: Update the feature 2-3 ‘PDSCH MIMO layers” in the RAN1 NR UE Feature as follows and inform RAN1 and RAN about the feature update.
  Proposal 2: Confirm the features ‘Almost contiguous UL CP-OFDM (feature 2-7)’ and ‘PA calibration gap (feature 2-8)’ as optional with capability signaling and inform RAN2 about RAN4’s decision
  Proposal 3: If needed, define further details to the ‘Almost contiguous UL CP-OFDM (feature 2-7)’ and ‘PA calibration gap (feature 2-8)’ features once the corresponding UE requirements are finalized.
  Proposal 4: RAN4 should discuss and decide how to capture the limitation that UL-MIMO is not supported in SUL carrier in Rel-15 and if any related UE capability signaling is needed for possible future introduction of UL-MIMO for SUL.
2-3 | PDSCH MIMO layers | 1. Supported maximal number of MIMO layers | Candidate values: {1,2,4,8} FFS on the minimal layers for different band or band combination. | For single CC standalone NR, it is mandatory with capability signaling to support at least 4 MIMO layers for all operating scenarios (EN-DC, CA, non-EN-DC/non-CA) in the bands where 4Rx is specified as mandatory for the given UE and at least 2 MIMO layers in FR2 for all operating scenarios (EN-DC, CA, non-EN-DC/non-CA). Some relaxations to this requirement may be applicable in the future (including in Rel-15). Mandatory in all cases means mandatory with capability signaling. It is not expected that there is a signaling change (i.e. signaling remains to be defined as {1, 2, 4, 8} in every band and every band combination, including FR1 and FR2 in all cases.

## Slide 17: MIMO layer related
Proposal for UL-MIMO in SUL carrier
  Send LS to RAN1 to inform the following RAN4 agreement
    It is agreed that UL-MIMO is not supported in SUL carrier in Rel-15
  RAN4 ask to RAN1 to include this decision into RAN1 feature list