## Slide 1: Way forward on Test Configurations for MSR
Ericsson, Nokia, Huawei, ZTE
R4-1811619
3GPP TSG-RAN WG4 Meeting #88 Gothenburg, Sweden, 20th – 24th August, 2018
Agenda item: 7.9.1

## Slide 2: Background
In RAN4#88, discussions started on conducted MSR testing (TS 37.141) with NR.
Contribution [1] listed proposals on topics to be investigated related to Test Configurations.
This Way Forward captures the different topics to be further investigated for next RAN4#88b meeting.
References:
[1] R4-1810087, “NR Test Configurations for MSR conformance tests”, Ericsson

## Slide 3: Way forward – Test signal
The test signal(s) used to build TCs to test CS16 and CS17 should be further investigated.
Initial proposal:
 | Lower edge | Upper edge
CS16 | Typical NR signal | E-UTRA 10MHz with NB-IoT in guard band E-UTRA 5MHz with NB-IoT in-band (Note 1) E-UTRA 5 MHz (Note 2)
CS17 | E-UTRA 10 MHz with NB-IoT in guard band E-UTRA 5MHz with NB-IoT in-band (Note 1) Typical NR signal (Note 2) | NB-IoT standalone
Note 1: if NB-IoT in guard band is not supported Note 2: if NB-IoT in-band and NB-IoT in guard band is not supported Note 3: Typical NR signal is 5MHz CBW and 15kHz SCS. In case 5/10MHz CBW is not supported, the smallest supported CBW is selected. |  | 

## Slide 4: Way Forward – Non Contiguous and Multi-band open issues
Current status:
  TS 37.141: No TC supports E-UTRA with NB-IoT in-band / guard band for:
    Non-Contiguous spectrum
    Multi-band operation
  TS 36/37.104: NB-IoT standalone is not supported for:
    Non-Contiguous spectrum
    Multi-band operation
Clarify if CS16 / CS17 should support:
  Non-Contiguous spectrum?
  Multi-band operation?

## Slide 5: Way Forward – List of TCs
Submit list of new TCs to be specified to test CS16 and CS17.