## Slide 1: WF on remaining issues for RRM testing methodology
3GPP TSG-RAN WG4 Meeting #88 R4-1811890
Gothenburg, SE, 20th – 24th Aug, 2018
Qualcomm Incorporated

## Slide 2: Methodology to derive SNR/SINR
Agreement from the Ad-hoc for RRM:
  Case of 1 AoA (signal and noise are transmitted from the same probe):
    Reuse methodology to derive the SNR at Reference point from UE Baseband SNR defined for UE demodulation test methodology under assumption that the testing is done under RX beam peak direction.
    Further discuss how to handle the case when the test is done not in RX beam peak direction
  Case of 2 AoAs:
    Further discuss the methodology to derive the SNR at Reference point from UE Baseband SNR
Proposals:
For case of 1 AoA, RAN4#88Bis will define the methodology to derive the SNR at Reference point from UE BB SNR under non-RX beam peak direction assumptions
  Signal and noise are transmitted from the same probe
  Consider the spherical coverage and antenna gain assumptions for non-Rx beam peak.
For case of 2 AoAs, RAN4#88Bis will define the methdology to derive specify the SNR/SINR at Reference point from UE BB SNR/SINR.
  Signal and noise can be transmitted from 2 probes one or both active probes. Test description will define the exact signal/noise/SNR/SINR level per TRxP at the reference point.
  Consider the spherical coverage and antenna gain assumptions for 2 AoAs.
Capture the methodology how to derive and control the SNR/SINR at reference point in 1 AoA and 2 AoAs cases in TR.

## Slide 3: Power, SNR/SINR Range
Proposals:
  In RAN4#88Bis: Identify approximate Power, SNR range under the RX beam peak direction and non-RX beam peak direction with 1 AoA
  In RAN4#88Bis: Identify the approximate Power, SNR/SINR range with 2 AoAs
  The difference between SNR at reference point and SNR at UE BB is [1]dB.
    Consider [1]dB of difference between SNR at reference point and SNR at UE BB as the starting point.
  Capture the SNR range for both 1 AoA and 2 AoAs cases in the TR.

## Slide 4: Testing methodology
Background:
  The testing methodology issues are identified in R4-1810563.
    The probes that can be used during the test will depend on the UE position and the actual spherical coverage.
Proposals:
  RAN4#88Bis will study how to define a map of the directions in which the UE RRM test cases will be definedmeets the spherical coverage requirement.
    Input from the TE vendors on whether the identification the map of the directions is feasible is needed.
    Companies are encouraged to provide input on how to identify the directions in which the UE RRM test cases will be defined can be performed.

## Slide 5: EIS spherical coverage
Background:
  The requirements of EIS spherical coverage will be defined in RAN4. But the methodology of how to test the EIS spherical coverage has not been studied in the SI.
  From UE RF Chairman’s minutes:
    Agreement: RAN4 specifies EIS spherical coverage requirement. How to test the requirement for UE with or without beam correspondence will be further discussed
Proposals:
  The methodology of how to test the EIS spherical coverage for UE with or without beam correspondence will be discussed from RAN4#88Bis in the UE RF session. And the methodology can be used for Rel-15 test cases. Testability experts are encouraged to contribute to the related discussion.
Notes: 1811522