## Slide 1: N12 REFSENS for 15 MHz channel
AI 7.1.1
Nokia
Discussion
R4-1812048

## Slide 2: Background
For LTE band 12 has 5 and 10 MHz channel bandwidths and for NR in addition 15 MHz.
REFSENS is same for LTE and NR except some scaling of BW
UL allocation for REFSENS is same for all cases i.e. 20 RB
BUT UL to DL separation for NR 15 MHz case is smaller that for 10 or 5 MHZ and that has not been taken into account, see figure below.
In next slides we compare NR 10 MHz channel emissions to own Rx band with 20 RB UL allocation to various 15 MHz NR signal emissions casue by different UL allocations.

## Slide 3: 15 MHz NR allocation in worst case position
If 15 MHz CH BW is placed traditionally to worst case position then IMD5 noise will be 14.1 to 18.4 dB more than 10 MHz channel noise to own receive band.
See the legend where 20RB@32 is CLRB=20 and RB start = 32

## Slide 4: 15 MHz NR allocation in same position as 10 MHz NR
If 15 MHz NR carrier uplink is placed to roughly similar position as 10 MHz NR carrier then as expected the noisee behaviour to own recieve band is similar.
Potential test point for 15 MHz could be
Clrb=20 and RB start = 34. Then there is no need to change current REFSENS but it is kind of cheating and gives too optimistic picture of the situation.