## Slide 1: WF for SSB-based RLM test cases in Rel-15
MediaTek Inc.
3GPP TSG-RAN WG4 Meeting #88-Bis
Chengdu, China, 8th – 12th Oct, 2018
Agenda Item: 7.12.5.13
Document for: Approval
R4-1812515

## Slide 2: Issues in RLM test cases (1)
Issue 1: RLM test cases in EN-DC. EUTRA is in non-DRX mode
A. 4.5.1.1 | FR1 | Non-DRX | FDD | OOS | w/o meas. gap | Test 1-A: SCS 15KHz, Test 1-B: SCS 30KHz
 |  |  |  |  | w/ meas. gap | Test 2-A: SCS 15KHz, Test 2-B: SCS 30KHz
A. 4.5.1.2 |  |  |  | INS | w/o meas. gap | Test 1-A: SCS 15KHz, Test 1-B: SCS 30KHz
 |  |  |  |  | w/ meas. gap | Test 2-A: SCS 15KHz, Test 2-B: SCS 30KHz
A. 4.5.1.3 |  |  | TDD | OOS | w/o meas. gap | Test 1-A: SCS 15KHz, Test 1-B: SCS 30KHz
 |  |  |  |  | w/ meas. gap | Test 2-A: SCS 15KHz, Test 2-B: SCS 30KHz
A. 4.5.1.4 |  |  |  | INS | w/o meas. gap | Test 1-A: SCS 15KHz, Test 1-B: SCS 30KHz
 |  |  |  |  | w/ meas. gap | Test 2-A: SCS 15KHz, Test 2-B: SCS 30KHz
 |  | DRX |  |  |  | 
A. 4.5.1.5 |  |  | TDD | OOS | w/o meas. gap | Test 1-A: SCS 15KHz, Test 1-B: SCS 30KHz
 |  |  |  |  | w/ meas. gap | Test 2-A: SCS 15KHz, Test 2-B: SCS 30KHz
A. 4.5.1.6 |  |  |  | INS | w/o meas. gap | Test 1-A: SCS 15KHz, Test 1-B: SCS 30KHz
 |  |  |  |  | w/ meas. gap | None
A. 4.5.1.7 |  |  | FDD | OOS | w/o meas. gap | Test 1-A: SCS 15KHz, Test 1-B: SCS 30KHz
 |  |  |  |  | w/ meas. gap | Test 2-A: SCS 15KHz, Test 2-B: SCS 30KHz
A. 4.5.1.8 |  |  |  | INS | w/o meas. gap | Test 1-A: SCS 15KHz, Test 1-B: SCS 30KHz
 |  |  |  |  | w/ meas. gap | None
A.5.5.1.1 | FR2 | Non-DRX | TDD | OOS | w/o meas. gap | Test 1: SCS 120KHz
 |  |  |  |  | w/ meas. gap | Test 2: SCS 120KHz
A.5.5.1.2 |  |  |  | INS | w/o meas. gap | Test 1: SCS 120KHz
 |  |  |  |  | w/ meas. gap | Test 2: SCS 120KHz
A.5.5.1.3 |  | DRX | TDD | OOS | w/o meas. gap | Test 1: SCS 120KHz
 |  |  |  |  | w/ meas. gap | Test 2: SCS 120KHz
A.5.5.1.4 |  |  |  | INS | w/o meas. gap | Test 1: SCS 120KHz
 |  |  |  |  | w/ meas. gap | None

## Slide 3: Issues in RLM test cases (2)
Issue 2: RLM test cases for SA
A. 6.5.1.1 | FR1 | Non-DRX | FDD | OOS | w/o meas. gap | Test 1-A: SCS 15KHz, Test 1-B: SCS 30KHz
 |  |  |  |  | w/ meas. gap | Test 2-A: SCS 15KHz, Test 2-B: SCS 30KHz
A. 6.5.1.2 |  |  |  | INS | w/o meas. gap | Test 1-A: SCS 15KHz, Test 1-B: SCS 30KHz
 |  |  |  |  | w/ meas. gap | Test 2-A: SCS 15KHz, Test 2-B: SCS 30KHz
A. 6.5.1.3 |  |  | TDD | OOS | w/o meas. gap | Test 1-A: SCS 15KHz, Test 1-B: SCS 30KHz
 |  |  |  |  | w/ meas. gap | Test 2-A: SCS 15KHz, Test 2-B: SCS 30KHz
A. 6.5.1.4 |  |  |  | INS | w/o meas. gap | Test 1-A: SCS 15KHz, Test 1-B: SCS 30KHz
 |  |  |  |  | w/ meas. gap | Test 2-A: SCS 15KHz, Test 2-B: SCS 30KHz
 |  | DRX |  |  |  | 
A. 6.5.1.5 |  |  | TDD | OOS | w/o meas. gap | Test 1-A: SCS 15KHz, Test 1-B: SCS 30KHz
 |  |  |  |  | w/ meas. gap | Test 2-A: SCS 15KHz, Test 2-B: SCS 30KHz
A. 6.5.1.6 |  |  |  | INS | w/o meas. gap | Test 1-A: SCS 15KHz, Test 1-B: SCS 30KHz
 |  |  |  |  | w/ meas. gap | None
A. 6.5.1.7 |  |  | FDD | OOS | w/o meas. gap | Test 1-A: SCS 15KHz, Test 1-B: SCS 30KHz
 |  |  |  |  | w/ meas. gap | Test 2-A: SCS 15KHz, Test 2-B: SCS 30KHz
A. 6.5.1.8 |  |  |  | INS | w/o meas. gap | Test 1-A: SCS 15KHz, Test 1-B: SCS 30KHz
 |  |  |  |  | w/ meas. gap | None
A.7.5.1.1 | FR2 | Non-DRX | TDD | OOS | w/o meas. gap | Test 1: SCS 120KHz
 |  |  |  |  | w/ meas. gap | Test 2: SCS 120KHz
A.7.5.1.2 |  |  |  | INS | w/o meas. gap | Test 1: SCS 120KHz
 |  |  |  |  | w/ meas. gap | Test 2: SCS 120KHz
A.7.5.1.3 |  | DRX | TDD | OOS | w/o meas. gap | Test 1: SCS 120KHz
 |  |  |  |  | w/ meas. gap | Test 2: SCS 120KHz
A.7.5.1.4 |  |  |  | INS | w/o meas. gap | Test 1: SCS 120KHz
 |  |  |  |  | w/ meas. gap | None

## Slide 4: Issues in RLM test cases (3)
Issue 3: RX beam sweeping in FR2 test cases (Strive to minimize the number of test case)
  Option 1: N= 1 only
Issue 4: consider the scenarios with intra frequency measurement without gap and/or gap based measurement in FR2 RLM test cases (Strive to minimize the number of test case)
  option 1: only gap based measurement (In FR2, SMTC is configured and fully overlapped with MG)

## Slide 5: Issues in RLM test cases (4)
Issue 5: BFR-triggered RLF Avoidance
  Option 1: largest preambleTransMax value, the longest periodicity of PRACH occasion and larger ra-ResponseWindow for BFR
    preambleTransMax = n200
    periodicity of PRACH occasion = 160ms
    ra-ResponseWindow = 1 slot for FR1 and 40 slots for FR2
Issue 6: failureDetectionResources and candidateBeamRSList configuration
  Option1: given by TCI states (not signaled by higher layers)
Issue 7: periodic PUCCH transmission
  Quantity:
    Option1: cri-rsrp
      Number of NZP CSI-RS resources within one NZP CSI-RS resource set for BM: TBD

## Slide 6: Issues in RLM test cases (5)
Issue 8: The number of SSB in FR2 RLM test (Note: single AoA is configured for RLM)
  Option 1: 1
  Option 2: 2
Issue 9: Reuse LTE RLM test methodology with some modifications
  OOS: Time difference between point B and point C (T4) shall equal to TEvaluate_out + 40 ms
  INS:
    T3 > TEvaluate_out
    T310 >= T3+T4+TEvaluate_in + SSB burst duration
    T6 > TEvaluate_out + T310 + 40 – T3 –T4

## Slide 7: Issues in RLM test cases (6)
Issue 10: SNR level determination
  Phase 0: Align required SNR_OOS and SNR_INS to achieve target OOS/INS hypothetical PDCCH performance (RAN4#88-bis)
    FR1 FDD/TDD SCS 15/30KHz, FR2 TDD SCS 120KHz
      TDD: Reuse same TDD pattern from REFSENS tests
    RLM-IS-OOS-thresholdConfig: Configuration #0 (Table 8.1.1-1 in TS 38.133)
    INS (Table 8.1.2.1-2 in TS 38.133) and OOS (Table 8.1.2.1-1 in TS 38.133)
      RMSI CORESET: RB: 24PRBs, time duration: 2 OFDM symbols, interleaved
      DCI payload size for DCI Format 1_0: 39
    Channel model: static
  Phase 1: Align radio link quality estimation performance. Determine SNR levels based on the results of link quality performance alignment(RAN4#89)
    SSB periodicity: 20 ms
    measurement gap: partially overlapped/non-overlapped, where MRRP is [40] ms
    SMTC periodicity for intra measurement without gap in FR2
    OOS: SNR_OOS = [TBD] dB, OOS evaluation period = TEvaluate_out_SSB
    INS: SNR_INS = [TBD] dB, INS evaluation period = TEvaluate_in_SSB