## Slide 1: Way forward on Test case list for MSG3 based channel quality report
Ericsson
3GPP TSG-RAN WG4 Meeting #88bis
Chengdu, China, 8 – 12 October, 2018
R4-1813670

## Slide 2: Agreements
RAN4 will specify the test case for NB-IoT MSG3-based channel quality reporting from Rel-14 (TEI14)
Test procedure:
  TE sets Es/Iot.
  TE receives CQI-NPDCCH-NB or CQI-NPDCCH-Short-NB depending on the RRC message
  TE transmits NPDCCH with repetition number R and verifies NPDCCH BLER does not exceed 1%.
  TE transmits NPDCCH with repetition number based on TS36.133 Table 9.1.22.16-1 and verifies NPDCCH BLER is larger than 1%.
Companies are encouraged to propose the test point for test cases in RAN4#89. (See next page)

## Slide 3: Agreed test cases
Test number | Test 1 | Test 2
Ês/Iot | More than -6dB, e.g. -4dB | Less than -6dB, e.g., -12dB
DCI format | N1 | N1
Antenna configuration | 2x1 | 2x1
Channel model | AWGN | AWGN
Aggregation level | 2 | 2
DRX | OFF | OFF
Channel quality IE | CQI-NPDCCH-NB | CQI-NPDCCH-NB