## Slide 1: 3GPP TSG-RAN WG4 Meeting #88Bis Chengdu, China, 08 – 12 October 2018
Huawei, …
Way forward on General part of NR BS demodulation performance
R4-1813755

## Slide 2: Background
The following WFs were approved:
  R4-1808022 Way forward on general part for NR BS demodulation requirements, RAN4#87
  R4-1809370 Way forward on general parameters for BS demodulation performance requirements, RAN4#AH1807
  R4-1811726 Way forward on general part of NR BS demodulation performance, RAN4#88

## Slide 3: General - 1
TDD UL/DL configurations
  Use one TDD UL/DL configuration per SCS
    15 kHz SCS
      3D1S1U, S=10D:2G:2U
    30 kHz SCS
      7D1S2U, S=6D:4G:4U
    60 kHz SCS
      DDDSU, S = 10D:2G:2U
    120 kHz SCS
      DDDSU, S=10D:2G:2U
  No PUSCH transmission on the special slot
Phase Noise
  FFS whether PN is modelled in FR2 simulation
    Option 1: Yes, and select one of the two options from the TR.
    Option 2: No, and add a certain amount of margin on top of the impairment results provided by companies. The exact margin to be added is up to company’s implementation.
  Further discuss whether to have carrier frequency specific requirements for FR2

## Slide 4: General - 2
Antenna configuration for FR1
  For conducted FR1 BS demodulation performance requirements: for FR1 NR BS with more than 8 antenna connectors/TAB connectors, apply the minimum demodulation performance requirements for 8 RX , the specific connectors used for testing are declared by the vendor as in eAAS specification.
  For OTA FR1 BS demodulation performance requirements: due to current AAS BS OTA test setup for 2Rx, independent fading and AWGN can only be achieved on using orthogonal polarizations. Thus the BS is illuminated with independent AWGN and fading per polarization and meets 2RX requirements. Mapping of connectors and demodulation branches is implementation dependent.
EN-DC:
  No specific tests for EN-DC in BS demodulation performance requirements in Rel-15.

## Slide 5: Channel Model
FR1 conducted
  Reuse the conclusions from UE demodulation discussions
FR1 and FR2 radiated
  Fading channel as well as AWGN can be applicable for BS OTA demodulation test. If fading channel is modeled for BS OTA demodulation test:
    As baseline, the fading channel is modelled via channel simulator outside of anechoic chamber (e.g., CATR or chamber) that is used for wireless cable replacement method